DFE-520TX

Date: March 15, 2005

| Product name: | DFE-520TX |
| --- | --- |
| Product Group & Type: |  |
| Revision: | A1 |
| Available: |  |
| Picture: |  |
| Why Sell This Product: | This network card is the lowest cost network card offered by D-Link. It provides the basic functions for desktop Ethernet connection (no WOL, no boot ROM). It’s target at users needing just the basic Ethernet connection. Selling Points Extremely low price. Single-chip solution for high hardware reliance. Small size, light weight. |
| Key Features: | 802.3 10BASE-T/802.3u 100Base-TX standard Auto-detection of 10Mbps and 100Mbps network speeds Supports 802.1x function (MD5 only) 32-bit PCI Local Bus Master high-speed operation Full/half duplex operation Complies with Advanced Configuration and Power Interface specification v.1.0 Complies with PCI Power Management v.1.1 Supports 802.3x Flow Control Supports PCI clock speed up to 33Mhz independent of network clock On-board FIFO buffer, no external memory on host required Low Ethernet command processing overhead |
| Technical Details: | General Standards - IEEE 802.3 10BASE-T Ethernet - IEEE 802.3u 100BASE-TX Fast Ethernet - IEEE 802.3 NWay auto-negotiation - IEEE 802.3x Flow Control - PCI local bus 2.2 specification Topology Star Protocol CSMA/CD Network Data Transfer Rates - 10BASE-T: 10Mbps (half-duplex) 20Mbps (full-duplex) - 100BASE-TX: 100Mbps (half-duplex) 200Mbps (full-duplex) Network Cables - 10BASE-T: UTP Cat.3, 4, 5 (100 m max.) EIA/TIA-568 STP (100 m max.) - 100BASE-TX: UTP Cat. 5 (100 m max.) EIA/TIA-568 STP (100 m max.) Diagnostic LED Report - Link - Activity Physical & Environmental Power Consumption 0.4 watts max. Dimensions 120 x 20 mm Weight 106 grams Operating Temperature 0 to 40 ℃ Storage Temperature -10 to 70 ℃ Operating Humidity 10% to 90% RH Storage Humidity 5% to 90% RH Emission - FCC Class B - CE Class B - C-Tick O.S. Driver Support Microsoft Windows 98 SE, 2000, ME, XP |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( CUL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box( Gift Box ( Bulk ( White Box with D-Link Logo ( Others |
| Packaging Contents: | DFE-520TX NIC card One CD Rom for Manual/QIG/Driver One hard copy QIG |
| UPC Code: | EFE520TX..A1 790069275562 IFE520TX..A1 790069275579 TFE520TX..A1 790069275586 NFE520TX..A1 790069275593 BFE520TX..A1 790069275609 |
| Units Per Carton: | 60 |
| Cartons Per Pallet: | For USA Air:12, Sea: 14 | For WW Air:16, Sea: 16 |
| Dimensions and Weight: | Box: mm,Others 160mm x 182mm x 20mm, 0.106 kg Carton: 590x457x480 mm, 10.01 kg Pallet: (by Air) 1220x1020x1453 mm, 136.2 kg (for USA) 1200x1100x2055 mm, 178.66 kg (for WW) (by Sea) 1220x1020x2050 mm, 176.16 kg (for USA) 1200x1100x2055 mm, 178.66 kg (for WW) INTRASTAT weight: 0.058 kg (Box) Packing material weight (Box): - Paper: 0.022 kg - Plastic: 0.017 kg - Mixed: 0.019 kg |

| PMA |
| --- |
| Product Class |  |
| Item Group |  |  |
| Sub Group |  |
| Intelligence |  |
| Tech.(Features) |  |
| Layer |  |  |
| Application |  |
| Q'ty |  |  |
| Interface |  |  |
| Net Interface |  |  |
| Port NO. |  |  |