How to configure DNS Relay

This example describes about firewalls support to relay DNS query packets from LAN to Internet for domain name resolving. All DFL firewalls (DFL-210/800/1600/2500) support this feature from firmware v2.04 and later.

Note: About this feature, it performs relay/forward DNS packets only since D-Link DFL firewalls don’t built-in DNS server in system kernel. Therefore, it can not instead of real DNS server to provide domain name resolving and related functionality.

Details:

- LAN IP on firewall: 192.168.1.1 (with the function of DNS relay)

- Lannet on firewall: 192.168.1.0/24

- DNS Server on Internet: 12.0.0.1

1. Addresses

Go to Objects -> Address book -> InterfaceAddresses

Create an IP Address called dns_server with address 12.0.0.1

Click Ok.

2. Create IP Rules to redirect DNS packets to Internet

Go to Rules -> IP Rules

Create a new IP Rule with SAT action.

In the General tab:

General:

Name: SAT_DNS_Relay

Action: SAT

Service: dns_all

Address Filter:

Source Interface: lan

Source Network: lannet

Destination Interface: core

Destination Network: lan_ip

In the SAT tab:

General:

Translate the: Destination IP Address

New IP Address: dns_server

Click Ok.

Create an identical IP Rule with NAT action. If the environment is not NAT, create a ALLOW rule instead.

In the General tab:

Name: Allow_DNS_Relay

Action: NAT

Service: dns_all

Address Filter:

Source Interface: lan

Source Network: lannet

Destination Interface: core

Destination Network: lan_ip

Click Ok.

Make sure these two rules are triggered before any generic rules (e.g. allow_standard rules).

And also, configure all PCs to have the firewall lan_ip (192.168.1.1) as DNS server.

Save and activate the configuration on firewall