How to configure High Availability (HA) mode on NetDefend Firewalls

This scenario shows how to configure NetDefend Firewalls in High Availability mode to provide a fault-tolerant capability that is available on DFL-1600 and DFL-2500. Details 
    for this scenario:

- Firewall A is the primary firewall as the Master

- Firewall B is the secondary firewall as the Slave

- Synchronization interface is on DMZ port connected via a cross-over cable.

- All the interfaces of the primary firewall need to be present on the backup firewall, and connected to the same networks.

- For each cluster interface, there are three IP addresses: two “real” IP addresses - one for each firewall; one “virtual” IP address – shared between the firewalls.

If the Master Firewall fails, the Slave Firewall will take over the jobs of the Master Firewall; thus network communication can be uninterrupted.

- Firewall A - Addresses

Go to Objects ->Address book -> InterfaceAddresses:

Edit the following items:

Rename dmz_ip as Virtual_dmz_ip and change IP address to 172.17.100.254

Rename dmznet as Virtual_dmznet and change IP address to 172.17.100.0/24

Rename lan1_ip as Virtual_lan1_ip and change IP address to 192.168.1.254

Rename lan1net as Virtual_lan1net and change IP address to 192.168.1.0/24

Rename lan2_ip as Virtual_lan2_ip and change IP address to 192.168.2.254

Rename lan2net as Virtual_lan2net and change IP address to 192.168.2.0/24

Rename lan3_ip as Virtual_lan3_ip and change IP address to 192.168.3.254

Rename lan3net as Virtual_lan3net and change IP address to 192.168.3.0/24

Rename wan1_ip as Virtual_wan1_ip and change IP address to 192.168.110.254

Rename wan1net as Virtual_wan1net and change IP address to 192.168.110.0/24

Rename wan1_gw as Virtual_wan1_gw and change IP address to 192.168.110.250

Rename wan2_ip as Virtual_wan2_ip and change IP address to 192.168.120.254

Rename wan2net as Virtual_wan2net and change IP address to 192.168.120.0/24

Create a new IP4 HA address for two real IP on DMZ Interface:

Name: HA-dmz

Master IP address: 172.17.100.253

Slave IP address: 172.17.100.252

Click Ok.

Create a new IP4 HA address for two real IP on Lan1 Interface:

Name: HA-lan1

Master IP address: 192.168.1.253

Slave IP address: 192.168.1.252

Click Ok.

Create a new IP4 HA address for two real IP on Lan2 Interface:

Name: HA-lan2

Master IP address: 192.168.2.253

Slave IP address: 192.168.2.252

Click Ok.

Create a new IP4 HA address for two real IP on Lan3 Interface:

Name: HA-lan3

Master IP address: 192.168.3.253

Slave IP address: 192.168.3.252

Click Ok.

Create a new IP4 HA address for two real IP on Wan1 Interface:

Name: HA-wan1

Master IP address: 192.168.110.253

Slave IP address: 192.168.110.252

Click Ok.

Create a new IP4 HA address for two real IP on Wan2 Interface:

Name: HA-wan2

Master IP address: 192.168.120.253

Slave IP address: 192.168.120.252

Click Ok.

- Firewall A - Ethernet interfaces

Go to Interfaces –> Ethernet:

Edit the dmz interface.

In the General tab:

General:

Leave IP Address as Virtual_dmz_ip and Network as Virtual_dmznet.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_dmz

Click Ok

Edit the lan1 interface.

In the General tab:

General:

Leave IP Address as Virtual_lan1_ip and Network as Virtual_lan1net.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_lan1

Click Ok

Edit the lan2 interface.

In the General tab:

General:

Leave IP Address as Virtual_lan2_ip and Network as Virtual_lan2net.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_lan2

Click Ok

Edit the lan3 interface.

In the General tab:

General:

Leave IP Address as Virtual_lan3_ip and Network as Virtual_lan3net.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_lan3

Click Ok

Edit the wan1 interface.

In the General tab:

General:

Leave IP Address as Virtual_wan1_ip, Network as Virtual_wan1net, and Default Gateway as Virtual_wan1_gw.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_wan1

Click Ok

Edit the wan2 interface.

In the General tab:

General:

Leave IP Address as Virtual_wan2_ip and Network as Virtual_wan2net.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_wan2

Click Ok

- Firewall A - Enable High Availability Configuration

Under System -> High Availability:

In the General tab:

General:

Select Enable High Availability

Cluster ID: 1

Sync Interface: dmz

Node Type: Master

Save and activate the configuration.

- Firewall B - Addresses

Go to Objects ->Address book -> InterfaceAddresses:

Edit the following items:

Rename dmz_ip as Virtual_dmz_ip and change IP address to 172.17.100.254

Rename dmznet as Virtual_dmznet and change IP address to 172.17.100.0/24

Rename lan1_ip as Virtual_lan1_ip and change IP address to 192.168.1.254

Rename lan1net as Virtual_lan1net and change IP address to 192.168.1.0/24

Rename lan2_ip as Virtual_lan2_ip and change IP address to 192.168.2.254

Rename lan2net as Virtual_lan2net and change IP address to 192.168.2.0/24

Rename lan3_ip as Virtual_lan3_ip and change IP address to 192.168.3.254

Rename lan3net as Virtual_lan3net and change IP address to 192.168.3.0/24

Rename wan1_ip as Virtual_wan1_ip and change IP address to 192.168.110.254

Rename wan1net as Virtual_wan1net and change IP address to 192.168.110.0/24

Rename wan1_gw as Virtual_wan1_gw and change IP address to 192.168.110.250

Rename wan2_ip as Virtual_wan2_ip and change IP address to 192.168.120.254

Rename wan2net as Virtual_wan2net and change IP address to 192.168.120.0/24

Create a new IP4 HA address for two real IP on DMZ Interface:

Name: HA-dmz

Master IP address: 172.17.100.253

Slave IP address: 172.17.100.252

Click Ok.

Create a new IP4 HA address for two real IP on Lan1 Interface:

Name: HA-lan1

Master IP address: 192.168.1.253

Slave IP address: 192.168.1.252

Click Ok.

Create a new IP4 HA address for two real IP on Lan2 Interface:

Name: HA-lan2

Master IP address: 192.168.2.253

Slave IP address: 192.168.2.252

Click Ok.

Create a new IP4 HA address for two real IP on Lan3 Interface:

Name: HA-lan3

Master IP address: 192.168.3.253

Slave IP address: 192.168.3.252

Click Ok.

Create a new IP4 HA address for two real IP on Wan1 Interface:

Name: HA-wan1

Master IP address: 192.168.110.253

Slave IP address: 192.168.110.252

Click Ok.

Create a new IP4 HA address for two real IP on Wan2 Interface:

Name: HA-wan2

Master IP address: 192.168.120.253

Slave IP address: 192.168.120.252

Click Ok.

- Firewall B - Ethernet interfaces

Go to Interfaces –> Ethernet:

Edit the dmz interface.

In the General tab:

General:

Leave IP Address as Virtual_dmz_ip and Network as Virtual_dmznet.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_dmz

Click Ok

Edit the lan1 interface.

In the General tab:

General:

Leave IP Address as Virtual_lan1_ip and Network as Virtual_lan1net.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_lan1

Click Ok

Edit the lan2 interface.

In the General tab:

General:

Leave IP Address as Virtual_lan2_ip and Network as Virtual_lan2net.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_lan2

Click Ok

Edit the lan3 interface.

In the General tab:

General:

Leave IP Address as Virtual_lan3_ip and Network as Virtual_lan3net.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_lan3

Click Ok

Edit the wan1 interface.

In the General tab:

General:

Leave IP Address as Virtual_wan1_ip, Network as Virtual_wan1net, and Default Gateway as Virtual_wan1_gw.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_wan1

Click Ok

Edit the wan2 interface.

In the General tab:

General:

Leave IP Address as Virtual_wan2_ip and Network as Virtual_wan2net.

In the Advanced tab:

High Availability:

Select Private IP Address as HA_wan2

Click Ok

- Firewall B - Enable High Availability Configuration

Under System -> High Availability:

In the General tab:

General:

Select Enable High Availability

Cluster ID: 1

Sync Interface: dmz

Node Type: Slave

Save and activate the configuration.