Configuration examples for the D-Link NetDefend Firewall series

DFL-210/800/1600/2500

Scenario: How to configure transparent mode in DHCP network environment

Last update: 2007-01-30

Overview

In this document, the notation Objects->Address book means that in the tree on the left side of the screen Objects first should be clicked (expanded) and then Address Book.

Most of the examples in this document are adapted for the DFL-800. The same settings can easily be used for all other models in the series. The only difference is the names of the interfaces. Since the DFL-1600 and DFL-2500 has more than one lan interface, the lan interfaces are named lan1, lan2 and lan3 not just lan.

The screenshots in this document is from firmware version 2.11.02. If you are using an earlier version of the firmware, the screenshots may not be identical to what you see on your browser.

To prevent existing settings to interfere with the settings in these guides, reset the firewall to factory defaults before starting.

Configuration examples for the D-Link NetDefend Firewall series

DFL-210/800/1600/2500

Scenario: How to configure transparent mode in DHCP network environment

Last update: 2007-01-30

Overview

In this document, the notation Objects->Address book means that in the tree on the left side of the screen Objects first should be clicked (expanded) and then Address Book.

Most of the examples in this document are adapted for the DFL-800. The same settings can easily be used for all other models in the series. The only difference is the names of the interfaces. Since the DFL-1600 and DFL-2500 has more than one lan interface, the lan interfaces are named lan1, lan2 and lan3 not just lan.

The screenshots in this document is from firmware version 2.11.02. If you are using an earlier version of the firmware, the screenshots may not be identical to what you see on your browser.

To prevent existing settings to interfere with the settings in these guides, reset the firewall to factory defaults before starting.

Configuration examples for the D-Link NetDefend Firewall series

DFL-210/800/1600/2500

Scenario: How to configure SAT (Port Forwarding) for DMZ server

Last update: 2007-01-30

Overview

In this document, the notation Objects->Address book means that in the tree on the left side of the screen Objects first should be clicked (expanded) and then Address Book.

Most of the examples in this document are adapted for the DFL-800. The same settings can easily be used for all other models in the series. The only difference is the names of the interfaces. Since the DFL-1600 and DFL-2500 has more than one lan interface, the lan interfaces are named lan1, lan2 and lan3 not just lan.

The screenshots in this document is from firmware version 2.11.02. If you are using an earlier version of the firmware, the screenshots may not be identical to what you see on your browser.

To prevent existing settings to interfere with the settings in these guides, reset the firewall to factory defaults before starting.

1

How to configure SAT(Port Forwarding) for DMZ server

In this example, we will create a SAT policy that will translate and allow connections from the Internet to a FTP server located in a DMZ

Example1: Wan 1 is used static ip

1. Addresses

Go to Objects -> Address book -> InterfaceAddresses.

Edit the following items:

Change Wan_ip to 192.168.174.70

Change Wannet to 192.168.174.0/24

Change lan_ip to 192.168.1.1

Change lannet to 192.168.1.0/24

2. Add the objects of both public and virtual IP addresses for FTP server

Go to Objects -> Address book -> InterfaceAddresses

Add a new IP Address

Name: FTP-virtual-ip

IP Address: 172.16.1.1

Click Ok

Add a new IP Address

Name: FTP-public-ip

IP Address: 192.168.174.71

Click Ok

3. Create the objects in ARP table

Go to Objects -> Interfaces -> ARP

Add a new ARP

Mode: Publish

Interface: wan1

IP Address: FTP-public-ip

Click Ok

4. Create the IP rule to map FTP server (SAT)

In the General tab:

Go to Rules -> IP Rules.

Add a new IP Rules

Name: FTP-map

Action: SAT

Service: ftp-inbound

Address Filter:

Source Interface: any

Source Network: all-nets

Destination Interface: wan1

Destination Network: ftp-public-ip

In the SAT tab:

Select Destination IP Address

New IP Address: FTP-vitual-ip

Click Ok.

Add a new IP Rules

Name: allow-FTP

Action: NAT

Service: ftp-inbound

Address Filter:

Source Interface: any

Source Network: all-nets

Destination Interface: wan1

Destination Network: ftp-public-ip

Click Ok.

Save and activate the configuration

2

How to configure SAT(Port Forwarding) for DMZ server

In this example, we will create a SAT policy that will translate and allow connections from the Internet to a FTP server located in a DMZ

Example2: Wan 1 is used PPPoE

1. Addresses

Go to Objects -> Address book -> InterfaceAddresses.

Edit the following items:

Change lan_ip to 192.168.1.1

Change lannet to 192.168.1.0/24

2. PPPoE client

Go to Interfaces -> PPPoE Tunnels.

Add a new PPPoE Tunnel.

In the General tab:

General:

Name: PPPoEClient

Physical Interface: wan1

Remote Network: all-nets

Authentication:

Username: dlink (For Example)

Password: dlink

Confirm Password: dlink

Click Ok.

2. Dynamic DNS

Go to System -> Misc. Clients.

Add a new DynDNSClientDynDNS.Org:

In the General tab:

DNSName: dlinktest.dyndns.org

Username: dlink

Password: dlink

Confirm Password: dlink

Click Ok.

3. Add the objects of both public and virtual IP addresses for FTP server

Go to Objects -> Address book -> InterfaceAddresses

Add a new IP Address

Name: FTP-virtual-ip

IP Address: 172.16.1.1

Click Ok

4. Create the IP rule to map FTP server (SAT)

In the General tab:

Go to Rules -> IP Rules.

Add a new IP Rules

Name: FTP-map

Action: SAT

Service: ftp-inbound

Address Filter:

Source Interface: any

Source Network: all-nets

Destination Interface: PPPoECleint

Destination Network: PPPoEClient_ip

In the SAT tab:

Select Destination IP Address

New IP Address: FTP-vitual-ip

Click Ok.

Add a new IP Rules

Name: FTP-map

Action: NAT

Service: ftp-inbound

Address Filter:

Source Interface: any

Source Network: all-nets

Destination Interface: any

Destination Network: PPPoEClient_ip

Click Ok.

Save and activate the configuration