How to Configure VLAN

This example requires a DFL-1600 or 2500 to be fully implemented. Most settings can however also be used on a DFL-210 or DFL-800.

Two tag based VLANs will be created on lan3, that connect to switch port with VLAN tag.

Details:

- From lan1, lan2 and lan3: HTTP, HTTPS and DNS connect to Internet via wan2.

- All internal nets can also access the Mail server in dmz.

- Only VLAN2 can access the FTP server in dmz.

1. Addresses

Go to Objects -> Address book -> InterfaceAddresses

Make sure the configured addresses match the following list, and add the objects that not already exist. To add new objects, select IP address from the add dropdown, enter name and address and click ok.

| Name | Address |
| --- | --- |
| lan1_ip | 192.168.1.1 |
| lan1net | 102.168.1.0/24 |
| lan2_ip | 192.168.2.1 |
| lan2net | 192.168.2.0/24 |
| lan3_ip | 192.168.3.1 |
| lan3net | 192.168.3.0/24 |
| dmz_ip | 172.17.100.254 |
| dmznet | 172.17.100.0/24 |
| wan1_ip | 192.168.110.1 |
| wan1net | 192.168.110.0/24 |
| wan1-gw | 192.168.110.254 |
| wan2_ip | 192.168.120.1 |
| wan2net | 192.168.120.0/24 |
| wan2-gw | 192.168.120.254 |
| vlan1_ip | 192.168.5.254 |
| vlan1net | 192.168.5.0/24 |
| vlan2_ip | 192.168.10.254 |
| vlan2net | 192.168.10.0/24 |
| ftp-server | 172.17.100.1 |
| mail-server | 172.17.100.2 |

Add a new IP4 Group.

In the General tab:

General:

Name: all-lannets

Add lan1net, lan2net, vlan1net and vlan2net.

Click Ok.

2. Ethernet interfaces

Go to Interfaces -> Ethernet.

Edit the wan1 interface to use the following settings.

In the General tab:

IP Address: wan1_ip

Network: wan1net

Default Gateway: wan1_gw

In the Advanced tab:

Automatic Route Creation:

Deselect Add route for interface network and Add default route if default gateway is specified.

Click Ok.

Edit the wan2 interface according to the following settings.

In the General tab:

General:

IP Address: wan2_ip

Network: wan2net

Default Gateway: wan2_gw

In the Advanced tab:

Automatic Route Creation:

Deselect Add route for interface network and Add default route if default gateway is specified.

Click Ok.

3. Routes

Go to Routing -> Routing Tables -> Main.

Add a new Route.

In the General tab:

General:

Interface: wan1

Network: all-nets

Gateway: wan1_gw

Local IP Address: (None)

Metric: 90

Click Ok.

Add a new Route.

In the General tab:

General:

Interface: wan2

Network: all-nets

Gateway: wan2_gw

Local IP Address: (None)

Metric: 80

Click Ok.

4. VLAN interfaces

Go to Interfaces -> VLAN.

Add a new VLAN.

In the General tab:

General:

Name: vlan1

Interface: lan3

VLAN ID: 1

Address Settings:

IP Address: vlan1_ip

Network: vlan1net

Default Gateway: (None)

Click Ok

Add a new VLAN.

In the General tab:

General:

Name: vlan2

Interface: lan3

VLAN ID: 2

Address Settings:

IP Address: vlan2_ip

Network: vlan2net

Default Gateway: (None)

Click Ok

5. Interface groups

Go to Interfaces -> Interface Groups.

Add a new Interface Group.

General:

Name: all-lan

Interfaces:

Add lan1, lan2, vlan1 and vlan2 to this group.

Click Ok.

Add a new Interface Group.

General:

Name: all-wan

Select Security/Transport Equivalent

Interfaces:

Add wan1 and wan2 to this group.

Click Ok.

6a. Rules to allow HTTP, HTTPS and DNS to Internet

Go to Rules -> IP Rules.

Add a new IP Rule (to allow outgoing HTTP).

In the General tab:

General:

Name: allow-http-all

Action: NAT

Service: http-all

Address Filter:

Source interface: all-lan

Source network: all-lannets

Destination interface: all-wan

Destination network: all-nets

Click Ok.

Add a new IP Rule (to allow outgoing dns).

In the General tab:

General:

Name: allow-dns-all

Action: NAT

Service: dns-all

Address Filter:

Source interface: all-lan

Source network: all-lannets

Destination interface: all-wan

Destination network: all-nets

Click Ok.

6b. Rules to allow internal users to access mail server

Add a new IP Rule (to allow internal smtp traffic to mailserver).

In the General tab:

General:

Name: allow-smtp-int

Action: Allow

Service: smtp

Address Filter:

Source interface: any

Source network: all-nets

Destination interface: dmz

Destination network: mail-server

Click Ok.

6d. Rules to allow traffic to FTP server from vlan2

Add a new IP Rule folder called vlan2_to_dmz.

Add a new IP Rule (to allow ftp from vlan2 to dmz).

In the General tab:

General:

Name: allow-ftp

Action: Allow

Service: ftp-passthrough

Address Filter:

Source interface: vlan2

Source network: vlan2net

Destination interface: dmz

Destination network: dmznet

Click Ok.

Save and activate the configuration