| Firmware Version: | V1.03.08 |
| --- | --- |
| Prom Code Version: |  |
| Published Date: | 2014/6/26 |

Content:

Upgrading Instructions:	2

New Features:	2

Problems Fixed:	2

Known Issues:	3

Related Documentation:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| V1.03.08 | 2014/6/26 | DCS-2310L | A1, A2 |
| V1.02.00 | 2013/7/29 | DCS-2310L | A1 |
| V1.01.10 | 2013/6/18 | DCS-2310L | A1 |

# Upgrading Instructions:

Follow the steps below to upgrade the firmware:

1. Download the latest firmware file from the D-Link website. The file is in .bin file format.

2. Log-in camera web UI and enter setup/Maintenance/Firmware upgrade

3. Click Browse… and specify the firmware file.

3. Click Upgrade. The camera starts to upgrade and will reboot automatically when the upgrade completes.

# New Features:

| Fireware Version | New Features |
| --- | --- |
| V1.03.08 | Update the mydlink agent to 2.0.17-b76 Support MP4 recording format Added Schedule Reboot function |
| V1.02.00 | Update the mydlink agent to 2.0.17-b18 Support 2-way audio function at portal and APP Support onvif test tool V12.06 Enhancements the low light image. |
| V1.01.10 | The Firmware is only supported by wizard v1.04.03 or above. Upgrade to UPnP v1.6.18. Remove the default account “guest” RTSP Authentication is default enable. |

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| V1.03.08 | Fixed the issue of ICR switch failed in schedule mode after device reboot. Modified that when pre/post event image is set as 0, the device should send off one snapshot. Modified FTP time-out to 240 seconds. Fixed the issue that the device isn’t deleted from mydlink after factory reset and re-connecting to Internet. Fixed the issue that failed to delete the first user info in the guest list. Fixed the issue that when SD memory size is full by recording, the e-mail notification isn’t sent off. Fixed the issue that mydlink account is cleared out after downgrading to the previous FW version. Fixed the issue that camera IP doesn’t update to DDNS. Modified the event setup that needs to create 2 media for 2 events. Fixed the issue of FTP access problem with special character “$” used for the first letter of account data. |
| V1.02.00 | Fixed the IPV6 Enable and change the http port the web server will crash. |
| V1.01.10 | Remove the default account “guest”. RTSP Authentication is default enable. |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |
| V1.03.08 | Spec change: G.726 audio codec wouldn’t be supported in FW v1.03 or later. |

# Related Documentation:

N/A