| Firmware Version: | V1.03_b8 |
| --- | --- |
| Prom Code Version: |  |
| Published Date: | 2014/3/12 |

Content:

Upgrading Instructions:	2

New Features:	2

Problems Fixed:	2

Known Issues:	3

Related Documentation:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| V1.03_b8 | 2014/3/12 | DCS-5020L | A1 |
| V1.02_b5 | 2013/9/25 | DCS-5020L | A1 |
| V1.01_b2 | 2013/5/28 | DCS-5020L | A1 |

# Upgrading Instructions:

Follow the steps below to upgrade the firmware:

1. Download the latest firmware file from the D-Link website. The file is in .bin file format.

2. Log-in camera web UI and enter setup/Maintenance/Firmware upgrade

3. Click Browse… and specify the firmware file.

3. Click Upgrade. The camera starts to upgrade and will reboot automatically when the upgrade completes.

# New Features:

| Fireware Version | New Features |
| --- | --- |
| V1.03_b8 | New mydlink agent 2.0.17-b40. Change the default FTP to passive mode Support Win8.1 + IE11 Change WPS led on 10 seconds after WPS succeed. Change LANDAP protocol’s password length to 0 – 32 characters Support Java 7 Update 51 SSL Certificate will be automatically self signed (regenerated) during initial configuration/factory reset. |
| V1.02_b5 | Update mydlink agent to v2.0.17-b28. Add user can configure interval setting for motion/sound detection of mail/ftp. |
| V1.01_b2 | Update mydlink agent to v2.0.17-b06. Update h.264 Activex to v1.0.0.12. Only allow 0-9, a-z, A-Z, “.”, “-“, “_” as the user account name. |

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| V1.03_b8 | Adjust sensor settings for sometimes video flash issue. Fixed sometimes incorrect ICR control. Fixed Lens move left/right/up/down incorrect from mydlink portal/app when mirror/flip is enabled Fixed sometimes bad frame issue. Fixed mydlink event (sound detection) timing issue. |
| V1.02_b5 | Fixed schedule time of motion detection/sound detection incorrect issue when start time > end time. Fixed h.264 streaming issue tested on ios6. Fixed IP task will be restarted issue on DHCP renew time. Fixed OSD disappear issue. NTP source port change to port 123. Adjust sensor settings. |
| V1.01_b2 | Fix the problem that mydlink Agent will run twice when the camera is connecting to DIR-850L using WPS Push button. Fixed OSD color issue Fixed the direction of P/T control panel incorrect issue when Flip/Mirror enabled |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |

# Related Documentation:

N/A