| Firmware Version: | V2.10.07 |
| --- | --- |
| Prom Code Version: |  |
| Published Date: | 2015/6/13 |

Content:

Upgrading Instructions:	2

New Features:	2

Problems Fixed:	3

Known Issues:	3

Related Documentation:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| V2.00_4017 | 2014/6/17 | DCS-942L | B1 |
| V2.10.07 | 2015/6/13 | DCS-942L | B1, B2 |

# Upgrading Instructions:

Follow the steps below to upgrade the firmware:

1. Download the latest firmware file from the D-Link website. The file is in .bin file format.

2. Log-in camera web UI and enter setup/Maintenance/Firmware upgrade

3. Click Browse… and specify the firmware file.

3. Click Upgrade. The camera starts to upgrade and will reboot automatically when the upgrade completes.

# New Features:

| Firmware Version | New Features |
| --- | --- |
| V2.00_4017 | The 1st FW version for DCS-942L rev.B1. FW cannot backward compatible with Ax FW mydlink agent v2.0.17-b61 Add sensitivity settings for light sensor on device Web GUI |
| V2.10.07 | Update mydlink agent to v2.0.19-b05 Support auto image setting switching mechanism for H/W B1 and B2 (or above) camera lens. (* H/W B2 or above only supports v2.10.07 or above) The SD card can be recognized properly when formatting SD card by selecting default allocation unit size on Windows OS To improve the image quality (NOTE: The image settings will be in effect after factory reset.) Support new NIPCA CGI “/admin/videoclip.cgi” for Video Clip function Refine the firmware version naming definition Remove the AVI file format from SD recording and Video Clip function Remove the Ad-Hoc function Update the digital signature for Windows Improve the wireless site survey function Add Bonjour “_nipca._tcp” service type |

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| V2.00_4017 | Fixed the issue that adhoc connection cannot be established after configuration. |
| V2.10.07 | Fixed the vulnerability of Onward security test. OnSec-VUZ-103-48001, TLS/SSL Server Supports Weak Cipher Algorithms. Disable SSLv3 Update the time zone table list for Russian and Chile. Fixed the NIPCA XML response issue by adding <root> tag as well-format. Correct the Content-Type for NIPCA APIs. Fixed the issue of false PIR trigger. Fixed the issue of low sensitivity for motion detection. Fixed the invisible SSID issue by adding wireless channel selector. Fixed the wireless connection failure issue when SSID/Key includes special character. |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |
| V2.10.07 | This firmware is compliant with DVC v3.6.4 + DP v1.6.13 and above |

# Related Documentation:

N/A