| Software Version: | 1.3-0329 |
| --- | --- |
| Prom Code Version: |  |
| Published Date: | 2011/06/22 |

Content:

Revision History and System Requirement:	2

New Features:	2

Problems Fixed:	3

Known Issues:	3

Related Documentation:	3

# Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| 1.3-0329 | 2011/06/22 | DCS-100/210/220/230 | N/A |

# New Features:

| Firmware Version | New Features |
| --- | --- |
| 1.3-0329 | 1. Support new camera: 1) DCS-940L (FW: 1.0.22) 2) DCS-6815 B1 (FW: 1.00.09) 3) DCS-6817 B1 (FW: 1.00.09) 4) DCS-6818 B1 (FW: 1.00.09) 5) DCS-6616 (FW: 1.00.09) 2. Change model name: 1) Change DCS-6815 to DCS-6815 A1 2) Change DCS-6817 to DCS-6817 A1 3) Change DCS-6818 to DCS-6818 A1 3. Remove old camera model: 1) DCS-6615 |

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| 1.3-0329 | 1. DCS-5230/ DCS-5230L It couldn't hear audio of DCS-5230(L) set SXGA video by D-ViewCam. 2. DCS-5300G It couldn't hear audio of DCS-5300G by D-ViewCam Modify result: >> Now supports audio on TCP protocol. >> Camera not supports audio through HTTP protocol. 3. DVS-310-1/ DCS-3415 When disable RS-485, D-ViewCam can still click PTZ control panel. Modify result: >> D-ViewCam will sync camera RS-485 status when first insert camera. If cameras don’t enable RS-485 in the first time inserting camera, the PTZ control panel will be grayed out. >> D-ViewCam can only sync RS-485 status when first inserting camera. D-ViewCam can’t sync on other situation like connect/reconnect or operating camera. |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |
| 1.3-0329 | 1. DCS-940L: D-ViewCam can’t get saturation value. (FW issue) 2. DCS-3110: D-ViewCam can’t set preset point. (FW issue) 3. DCS-681x B1: When choosing PTZ control panel: “Top-Left” or “Down-Left”, it will only move to left; When choose “Top-Right” or “Down-Right”, the Top and Down step is small. >> Please modify the “Tilt” speed into four times of “Pan” speed so that they can be balanced. (FW issue) 4. Don’t support Auto-Pan function for all camera models. 5. DCS-3710/6510/6511/DVS-210-1/DVS-310-1 >> When use MPEG4, users can’t set Bitrate and Quality at the same time. (CGI issue) 6. DCS-930/930L: >> When DCS-910 put several hours, it will be disconnected, but Web UI won’t. 7. DCS-6510 >> When use MPEG4 with 320x240 resolution, there’s low probability to have split screen. (version:1.02, firmware issue.) 8. DCS-3710 >> The settings of enable/ disable microphone/speaker cannot be synchronized between the system and the camera web page. (version: 1.00, firmware issue; FW V1.1 fixed) >> In MPEG4 mode, end users cannot modify option quality through Main console. (SDK issue) >> Bitrate value couldn't be shown correctly on DCS-3710 web interface. (version: 1.00.21, firmware issue; FW V1.1 fixed) >> The audio from DCS-3710 in D-ViewCam v3.11_0720 is unclear.(HW Known issue) >> When enable talk function by D-ViewCam v3.11_0720, the audio from speaker connected to DCS-3710. (HW Known issue) 9. DCS-6615/6815A1/ 6817 A1/ 6818 A1 >> Now all preset points are opened. >> The Mac address is incorrect from the device. (version: 1.01.03, firmware issue) >> If camera web UI is in auto focus mode, rather than manual focus mode, D-ViewCam can’t do focus. 10. DCS-2120 >> Mirror and flip function is not integrated into Main console. (D-ViewCam doesn't support this function) >> B/W mode is not integrated into Main console. (D-ViewCam doesn't support this function) >> Variable bitrate is not integrated into Main console. (D-ViewCam doesn't support this function) 11. DCS-3430/3411 >> Cannot choose the smallest resolution. (version: 1.02.4012, firmware issue; FW 1.02_4125 fixed) 12. DCS-5605/5635 >> Camera will back to “home” if clicking preset points. (version: 1.01.4023, firmware issue; FW 1.01_4126 fixed) >> When DCS-5605/5635 patrol, it didn't get in the preset points by D-ViewCam. 13. DCS-310 >> D-ViewCam couldn't catch DVS-310 frame rate information at first time to modify. (FW issue.) 14. DCS-3410, DCS-3411, DCS-3430, DCS6410, DCS-7410 and DCS-7510 >> D-ViewCam set preset point menu show incompletely on the DCS-3410, DCS-3411, DCS-3430, DCS6410, DCS-7410 and DCS-7510. (Design issue) |

# Related Documentation:

N/A

# Note:

HW Support List for Device Pack 1.3.0_20110329:

| Device | DCS-910 | DCS-920 | DCS-930 | DCS-930L | DCS-1100 | DCS-1100L | DCS-1130 | DCS-1130L | DCS-2102 | DCS-2120 | DCS-2120(TW) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Name |  |  |  |  |  |  |  |  |  |  |  |
| Final FW | 1.04_build_5 | 1.04_build_5 | 1.00 build 9 | 1.00 build 9 | 1.02_3522 | 1.03_4130 | 1.02_3522 | 1.03_4130 | 1.04_3227 | 1.04_3227 | 2.01tw |
| Device | DCS-2121 | DCS-3110 | DCS-3410 | DCS-3411 | DCS-3415 | DCS-3420 | DCS-3430 | DCS-3710 | DCS-5220Ax | DCS-5220Bx | DCS-5220(TW) |
| Name |  |  |  |  |  |  |  |  |  |  |  |
| Final FW | 1.04_3227 | 1.02 | 1.01_2812 | 1.02_4125 | 1 | 1.03 | 1.02_4125 | 1 | 1.05 | 2 | 2.00tw |
| Device | DCS-5230 | DCS-5230L | DCS-5300 | DCS-5300G | DCS-5605 | DCS-5610 | DCS-5635 | DCS-6110 | DCS-6111 | DCS-6410 | DCS-6620 |
| Name |  |  |  |  |  |  |  |  |  |  |  |
| Final FW | 1.02_4317 | 1.02_4317 | 1.06 | 2.05 | 1.01_4126 | 1.01 | 1.01_4126 | 1 | 1 | 1.00_3014 | 1.06 |
| Device | DCS-6620G | DCS-6510 | DCS-6511 | DCS-6616 | DCS-6815 A1 | DCS-6817 A1 | DCS-6818 A1 | DCS-7110 | DCS-7410 | DCS-7510 | DVS-210-1 |
| Name |  |  |  |  |  |  |  |  |  |  |  |
| Final FW | 1.05 | 1.02 | 0.08 | 1.00.09 | 1.01 | 1.01 | 1.01 | 1.00 | 1.00_3710 | 1.00_3909 | 1.00.01 |
| Device | DVS-310-1 | DCS-932 | DCS-932L | DCS-940L | DCS-6815 B1 | DCS-6817 B1 | DCS-6818 B1 |  |  |  |  |
| Name |  |  |  |  |  |  |  |  |  |  |  |
| Final FW | 1.02 | 1.00 | 1.00 | 1.0.22 | 1.00.09 | 1.00.09 | 1.00.09 |  |  |  |  |