DNS-120

Date: March 11, 2005

| Product name: | Network Storage Adapter |
| --- | --- |
| Revision: | A2 |
| Available: | 2005/02/25 |
| Picture: |  |
| Why Sell This Product: | We have released a storage product line, which included the flash drives and the network storage devices (with or without hard drives installed inside). Now, we’re adding to this product line a network storage adapter with only USB ports so users can plug in their flash drives and hard drive for network sharing. It’s cheap, and is a compact box for users who already have flash drives and external hard disks. This device is targeted at home consumers and SOHO users. Selling Points Very simple setup, no software installation required. Small, inexpensive device but includes the useful features like built-in FTP server to access files over Internet, search utility for quick discovery of drives on the network, access security and schedule file backup. |
| Key Features: | Allows 2 USB hard drive or flash drive connections 10/100 Ethernet LAN port with auto-MDI/MDIX Built-in FTP server to access files over Internet Easy search utility for quick discovery and mapping drives DHCP compatible No software installation necessary Web configuration utility User management Folder management USB drive to drive backup Local PC to USB drive backup Recurring and incremental backup Firmware upgrade utility *Unless additional precautions are taken, use of an FTP Server to access files over the Internet does not provide for secure or encrypted transmissions. It is recommended that the end-user utilize a Virtual Private Network (VPN) to establish a secure FTP session. Failure to properly disconnect USB drive may result in data loss and/or damage to the device. |
| Technical Details: | Standard - IEEE 802.3/802.3u Ethernet - USB 1.1, 2.0 - Samba 2.2.8a Device Interfaces - 1 10/100BASE-TX Ethernet with auto MDI-X support - 2 USB 2.0 ports Buttons - Disconnect button - Reset button DHCP Client Get IP address from DHCP server, Auto-IP Device Management - Windows-based utility with firmware download feature - Network settings - Auto IP capability - User account management - Folder and drive management - FTP server - Schedule download - Backup function Security Features - Folder permissions - Account-based access to FTP - Account-based access to scheduled downloads Security Methods - IP address filtering for Ethernet access with either Deny or Allow setting - In account mode, via username/password to access the assigned directory System Monitoring System log File System Type FAT 16/FAT 32 LED Indicators - Power - Ethernet - USB Diagnostics Capability - Power-on self test of flash memory, DRAM, Ethernet and USB ports - Syslog: 256 items Firmware Download Via Ethernet (error recovery mechanism must be in place) Physical & Environmental Power Requirement 5V DC, 2.5 A Power Supply Through external power adapter Dimensions 141 x 108 x 30 mm Weight 194 grams Operating Temperature 5 to 50 ℃ Storage Temperature -20 to 50 ℃ Operating Humidity 10% to 90%, non-condensing Storage Humidity 5% to 95%, non-condensing EMI - FCC Class B - CE - C-Tick Box Includes - DNS-120 Network Storage Adapter - Cat. 5 Ethernet cable - External power adapter - CD-ROM containing software and User s Manual - Quick Installation Guide |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( White Box with D-Link Logo ( Others |
| Packaging Contents: | DNS-120 Network Storage Adapter CAT5 Ethernet Cable Power Adapter ( 5V, 2.5A ) CD-ROM with Software and Manual Quick Installation Guide |
| UPC Code: | BNS120A…A2 790069 270666 ENS120B…A2 790069 271366 ENS120E…A2 790069 271373 INS120A…A2 790069 271380 INS120E…A2 790069 271397 INS120N…A2 790069 271403 CNS120A…A2 790069 274244 NNS120C...A2 790069 276644 |
| Units Per Carton: | 10 |
| Cartons Per Pallet: | For USA Air:27, Sea: 36 | For WW Air:27, Sea: 36 |
| Dimensions and Weight: | Box: ,Others , 0.86 kg Carton: 380 x 315 x 465 mm, 8.6 kg Pallet: (by Air) 1220 x 1020 x 1620 mm, 260 kg (for USA) 1200 x 1100 x 1620 mm, 260 kg (for WW) (by Sea) 1220 x 1020 x 1990 mm, 340 kg (for USA) 1200 x 1100 x 1990 mm, 232.2 kg (for WW) INTRASTAT weight: 0.86 kg (Box) Packing material weight (Box): - Paper: 0.632 kg - Plastic: 0.18 kg - Mixed: 0.07 kg |