DNS-300

Date: September 7, 2005

| Product Description: | Network Attached Storage |
| --- | --- |
| Revision: | A1 |
| Availability: | Now |
| Picture: |  |
| Why Sell This Product: | The new DNS-300 supplements the current DNS-312H network attached storage (NAS), which has a fixed size hard drive inside. This new product provides some flexibility -- an open bay for a 3.5-inch hard drive. Hard drive installation is left to the users, so sellers are spared of the trouble of keeping an inventory of hard drives. A built-in print server function allows users to attach a printer to the USB ports. Integrated FTP server allows for hard drive /file sharing on the network. This product is targeted at home and small office users. Selling Points - Home/SOHO NAS device that is easy to use, but has many of the little additional things that should make users happy, like Syslog with Network Time Protocol support, warning LED in case hard disk is full or broken, and e-mail notification of events/system errors. - Open bay for a flexible, user-installable hard drive. - Print server function included. - Disk drive folders can be easily organized, user access security provided. - Operates in multiple environments, including Windows, Linux and MacOS. |
| Key Features: | Hardware - 3.5-Inch Hard Drive Bay (IDE Interface) - 2 USB 2.0 Ports for Printer, External Hard Drive, Flash Drive Connection - 10/100BASE-TX Ethernet Port for Network Connection Built-in Functions - Integrated O.S., No Software Installation Required - Integrated Printer Server/FTP Server Security - User Account Database - Sharing of Folder Access Control by Single User or Groups - System Log With NTP (Network Time Protocol) Support - Warning LED in Case Hard Disk Full or Broken - E-Mail Notification of Important Events/System Errors Installation/Operation - Operates in Windows, Linux, MacOS Environments - UPnP AV Support for Easy Configuration With Other Audio/Video Equipment - System Configuration File Backup - Windows-Based Search/Configuration Utility |
| Technical Details: | Device Hardware - 3.5-inch hard drive bay (no hard drive included) - RISC processor - IDE interface to hard drive - Reset button External Interfaces - 2 USB 2.0 ports - 10/100BASE-TX Ethernet port Memory - Flash: 8MB - SDRAM: 64MB Software - Hard drive status and usage monitoring - Support DHCP client/server - Built-in print server (printer connection through USB 2.0 port) - External hard drive connection through USB 2.0 port - Built-in FTP server - UPnP AV support Print Server Support - Windows NT 4.0, ME, 2000, XP - MacOS - Linux OS Installation Utility Support - Windows NT 4.0, ME, 2000, XP Security - User Account database - Share folder access control by single user or groups and guests System - System configuration file backup - E-mail notification - System log - NTP (Network Time Protocol) Interoperability Multi-protocol system support on Windows, MacOS, Linux Driver/Firmware Support - Web based configuration - Windows-based setup utility Power Voltage 12VDC 3.3A Power Supply Through external power adapter Ventilation 12V DC fan |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( IC No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( CB No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( Brown Box ( Others |
| Packaging Contents: | One DNS-300 Device Quick Installation Guide Master CD Cat.5 cable 1.8M Power adapter (12V3.3A) |
| UPC Code: | UPC code Part Number 790069 281440 TNS300A...A1 790069 280498 INS300B...A1 790069 281150 ENS300B...A1 790069 281167 ENS300E...A1 790069 273223 INS300A...A1 790069 273230 INS300E...A1 790069 273247 INS300N...A1 790069 273612 NNS300C...A1 |
| Units Per Carton: | For WW |  |  |
|  | 4 |  |  |
| Cartons Per Pallet: | For WW |  |  |
|  | Air:30, Sea: 42 |  |  |
| Dimensions and Weight: | Box: ( 237x168x36mm (Type A) ( 225x150x75mm (Type B) ( 269x162x65mm (Type C) ( 274x208x68mm (Type D) ( 274x208x118mm (Type D1) ( 274x208x138mm (Type D2) ( 288x245x66mm (Type E) ( Others _315x235x125 mm_, 1.94 kg Carton: 537 x 338 x 271 mm, 8.8 kg Pallet: (by Air) 1200 x 1100 x 1480 mm, 279 kg (for WW) (by Sea) 1200 x 1100 x 2020 mm, 385 kg (for WW) INTRASTAT weight: 1.51 kg (Box) Packing material weight (Box): - Paper: 0.39 kg - Plastic: 0.068 kg - Mixed: 0.02 kg |