DES-3526/DES-3550

Date: March 11, 2004

| Product Model | DES-3526 | DES-3550 |
| --- | --- | --- |
| Product name: | 24 10/100Mbps plus 2 Gigabit ports Layer 2 switch | 48 10/100Mbps plus 2 Gigabit ports Layer 2 switch |
| Product Group & Type: | Gigabit Switch |
| Revision: | A1 |
| Available: |  |
| Picture: |  |
| Why Sell This Product: | D-Link's first Virtual Stack with Single IP Management, to compete against 3Com, Cisco, HP, etc. Better price than 3Com, Cisco, HP, etc. Make D-Link a leading Taiwan vendor of stackable switches with Single IP Management. Together with Single IP Management upgrade for other D-Link core switches in the near future, you will have a very complete Virtual Stack solution encompassing 10/100 departmental connection to L3 core switches to sell to large business & corporate users. Selling Points Enlarged & most complete software suite. Most complete security & QoS management set. Very comprehensive embedded web-based management software, much easier to use than SNMP software, but is free of charge! Very competitive price/performance/function ratio. Very high port density in a 1U rackmount box (DES-3550). |
| Key features: | Choices of 24 and 48 10/100BASE-TX ports per switch 2 combo 1000BASE-T/SFP Gigabit uplinks per switch Virtual stacking of up to 32 units per stack Up to 13.6Gbps backplane bandwidth Complete network access management solution Multi-layer (L2, L3, L4) Quality of Service Advanced Access Control Lists (ACL), enhanced TACACS+ and RADIUS* authentication 802.3ad LACP Link Aggregation port trunks IGMP snooping for multimedia applications CLI, Web-based and SNMP management, RMON monitoring Optional redundant power support * RADIUS support available in future firmware upgrade |
| Technical Details: | Hardware Number of Ports - DES-3526: 24 10/100BASE-TX ports, 2 combo 1000BASE-T/SFP - DES-3550: 48 10/100BASE-TX ports, 2 combo 1000BASE-T/SFP Port Standard/Function Support - IEEE 802.3 10BASE-T/802.3u 100BASE-TX - IEEE 802.3ab 1000BASE-T/802.3z 1000BASE-SX/LX - ANSI/IEEE 802.3 NWay auto-negotiation - IEEE 802.3x Flow Control - Auto MDI/MDIX SFP Support - IEEE 802.3z 1000BASE-LX (DEM-310GT transceiver) - IEEE 802.3z 1000BASE-SX (DEM-311GT transceiver) - IEEE 802.3z 1000BASE-LH (DEM-314GT transceiver) - IEEE 802.3z 1000BASE-ZX (DEM-315GT transceiver) Software VLAN - IEEE 802.1Q Tagged VLAN - Port-based VLAN - GARP/GVRP - Maximum number of VLANs per device: 255 static VLANs Priority Queues (CoS) - Standard: IEEE 802.1p - Number of queues: 4 Traffic Classification (CoS) Can be based on user-definable application types: - TOS - Diffserv (DSCP) - Port-based - MAC address - IP address - TCP/UDP port number Access Security - 802.1x port-based access control - 802.1x MAC-based access control - Port security - SSH v.1, v.2 * - SSL * * Functions available in future firmware upgrade Access Control List Multi-layer ACL based on: - Port number - TOS - Diffserv (DSCP) - MAC address - IP address - Packet protocol type - TCP/UDP port number (user-definable application types) - TCP/UDP payload (user-definable packet content) - Per port ACL definition Spanning Tree Protocol - 802.1D Spanning Tree compatible - 802.1w Rapid Spanning Tree - 802.1s Multiple Spanning Tree * * Function available in future firmware upgrade IP Multicast - IGMP Snooping - IGMP v.3 * * Function supported in future firmware upgrade Port Trunk - Maximum number of ports per trunk: 8 - Maximum number of trunks per device: 6 (DES-3526), 6 (DES-3550) - Operation mode: load sharing - 802.3ad compatible Link Aggregation (LACP) static & dynamic modes Performance Enhancement Functions - Traffic segmentation - Bandwidth control Performance Switch Fabric - DES-3526: 8.8Gbps - DES-3550: 13.6Gbps Packet Forwarding Rate - DES-3526: 6.6Mpps - DES-3550: 10.1Mpps Transmission Method Store-and-forward MAC Address Table - DES-3526: 8K entries per device - DES-3550: 8K entries per device MAC Address Learning - Dynamic entries: automatic update - Static entries: user-defined Packet Buffer Memory - DES-3526: 16Mbytes per device - DES-3550: 64Mbytes per device Configuration & Management Management Support - Single IP Management v.1 - SNMP v.1, v.2c, v.3 - Web-based management - Web GUI traffic monitoring - Web-based MAC address browsing - CLI (command line interface) - RMON monitoring - Telnet server (up to 8 sessions) - TACACS+ authentication on switch admin access - RADIUS authentication on switch admin access * - SYSLOG - DHCP/Bootp relay - DNS relay - Dual Images - Back-Door function - Web GUI traffic monitoring - Web MAC address browsing - Port description - CPU utilization monitoring * Function available in future firmware upgrade MIBs - MIB-II (RFC 1213) - Bridge MIB (RFC 1493) - RMON MIB (RFC 1757) - 802.1p Priority Queues (RFC 2674) - 802.1Q VLAN MIB (RFC 2674) - IGMP MIB (RFC 2833) - IF MIB (RFC 2233) - Ethernet-like MIB (RFC 1643) - D-Link enterprise MIB RMON Groups 1, 2, 3, 9 (Alarm, Statistics, History, Event) IP Number Self-identification Through DHCP client, Bootp client Firmware Upgrade TFTP Console Port DB-9 RS-232 DCE Physical & Environmental LED Indicators Per Device: - Power - Console - RPS Per Port: - 10/100Mbps - GE Power Supply 100 to 120 VAC, 200 to 250 VAC, 50 to 60 Hz Internal universal power supply Redundant Power Backup Support Connector to external RPS Power Consumption - DES-3526: 23 watts (max.) - DES-3550: 40 watts (max.) Ventilation - DES-3526: 40mm x 40mm DC fan x 1 - DES-3550: 40mm x 40mm DC fan x 2 Dimensions - DES-3526: 441 x 207 x 44 mm (device only) - DES-3526: 441 x 309 x 44 mm (device only) 19-inch rack-mount width, 1U height Weight - DES-3526: 2.56 kg (device only) - DES-3550: 4.4 kg (device only) Operating Temperature 0 to 40 (C Storage Temperature -40 to 70 (C Humidity 5% to 95% non-condensing Emission (EMI) - FCC Class A - CE Class A - C-Tick Safety CSA International |
| EMI/EMC Report | (FCC No. ( CE&RTTE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( Others |
| Packaging Contents: | One DES-3526 Device One set accessory including 2 Rack mount ear/4 Rubber feet and 8 Screws One AC power cord One Cable Ass’y RS232(DB09) One CD Kit for User’s Guide/CLI/D-View module One CD Kit for D-View 5.1 Trial vers. One Generic QIG | One DES-3526 Device One set accessory including 2 Rack mount ear/4 Rubber feet and 8 Screws One AC power cord One Cable Ass’y RS232(DB09) One CD Kit for User’s Guide/CLI/D-View module One CD Kit for D-View 5.1 Trial vers. One Generic QIG |
| UPC Code: | DES-3526 DES-3550 DES3526A..A1 790069265969 DES3550A..A1 790069266317 DES3526B..A1 790069265976 DES3550B..A1 790069266324 DES3526BE.A1 790069266010 DES3550BE.A1 790069266355 DES3526CN.A1 790069266669 DES3550CN.A1 790069266362 DES3526E..A1 790069265983 DES3550E..A1 790069266331 DES3526N..A1 790069265990 DES3550N..A1 790069266348 DES3526U..A1 790069266003 |
| Units Per Carton: | 5 | 3 |
| Cartons Per Pallet: | Air:60, Sea:120 | Air: 48, Sea: 72 |
| Dimensions and Weight: | Box: 554 x 306 x 92 mm, 3.64 kg Carton: 575 x 333 x 503 mm, 18.2 kg Pallet: Air: 1200 x 1100 x1120 mm, 255 kg Sea: 1200 x 1100 x2120 mm, 495 kg INTRASTAT weight: kg (Box) Packing material weight (Box): - Paper: kg - Plastic: kg - Mixed: kg | Box: 586 x 444 x 94 mm, 4.4 kg Carton: 605 x 462 x 309 mm, 13.2 kg Pallet: Air: 1200 x 1100 x1400 mm, 322.2 kg Sea: 1200 x 1100 x2040 mm, 475.8 kg INTRASTAT weight: kg (Box) Packing material weight (Box): - Paper: kg - Plastic: kg - Mixed: kg |