# DES-6500 Firmware Release Note

Firmware: R1.30-B02 (Runtime), B1.50-B19 (Prom)

Hardware: A1

Date: January 24, 2005

Problems Resolved:

No bug fixed in this version

Enhancements:

1. Add DES-6504 Line card support

2. Support Port description

3. Support CPU utilization monitoring

4. Support per port ACL, 100 ACL rules for each port

Warning:

1. The whole DES-6500 system must be upgraded to same version number of runtime code.

2. It is necessary that upgrade your system to R1.20-B09 before upgrade to R1.30-B02.

Firmware: R1.20-B09 (Runtime), B1.50-B19 (Prom)

Hardware: A1

Date: December 03, 2004

Problems Resolved:

- Solve the problem that multicast traffic was found packet loss while sending more than 210 multicast streams with wirespeed over PIM distribution.

- Solve the problem while distributing multicast traffic via DVMRP, packet will lose while sending wirespeed multicast streams and meanwhile there's IGMP join & leave.

- Solve GVRP update wasn't complete if the networks were built in loop topology.

- Solve packet lose problem when multicast streams were distributed via multicast routing protocol in L3 loop architecture.

- Solve GuangZhou HW Default Route Issue: While setting a default route, DES-6500 will learn each destination IP address and write it into ARP table. When ARP table is full, packets which destination is not learned will be send to CPU for software routing. This caused the CPU utilization high.

- Solve GuangZhou Virus Attack Issue: Virus packets will be sent to CPU due to LookUp Fail, but DES-6500 ACL cannot filter the LookUp Fail reason packets. It makes DES-6500 CPU utilization very high.

- Correct Web UI display error: QoS Class ID error in QoS scheduling Mechanism Table, Transmitted(TX) error in packet monitoring chart.

- Solve GVRP state can not save after saving configuration and reboot.

- Correct the error message on the first time boot up or after a factory reset.

- Solve the problem that DES-6500 (with DES-6507) perform NFS for file transfer between two difference subnet when DES-6500 configure as L3 Switch.

Enhancements:

- Add DES-6508 line card support

- Add DES-6510 line card support

- Support VRRP function

- Support HW default route

===== F/W Ver. 1.01-B40 (July, 2004) ==============================================

New features:

Add DES-6505 Line card support

Fixed:

- Multicast software routing

- PIM-DM multiple path, Link down the original path, it will not choose another one.

- Download configuration of 4k vlan, device will reboot

===== F/W Ver. 1.01-B26 (June, 2004) ==============================================

- First release version, support DES-6507/DES-6509 line cards. For the function/features, please refer to the Manual or datasheet.

- When upgrading, upgrade the line cards firmware and then CPU board firmware. Line cards and CPU board must have the same firmware version.