DGS-3324SRi

Date:   Oct. 28, 2003

| Product name: | 24-port 1000Base-T with 8 SFP Combo ports L3 Managed Stackable Switch |
| --- | --- |
| Product Group & Type: | D-Link redundant power supply system |
| Revision: | A1 |
| Available: | 2003/12/15 |
| Picture: |  |
| Why Buy This Product: | More enterprise solutions from D-Link: the DGS-3324SRi is an example of yet another Gigabit enterprise solution, with L3 routing support, rich in functions and reliable star stacking/RPS support. Star stacking solution for DGS-3224SR stackable Gigabit switches: L3 backbone attachment, L2 star stacking for DGS-3224SR. Similarity in technical support: this switch uses the same firmware as many of our L3 switches, so it should be easier for you to support. Selling Points Reliable star stacking architecture. Dual functions: this DGS-3312SRi can act both as a Gigabit switch, and a Stacking Master, at the same time. High port density/low-cost per port: 24 Gigabit ports in a low-profile stackable housing, plus 8 SFP ports. More and better software functions. Good price/performance/function ratio. |
| Keyfeatures: | Multi-layer L2/L3 packet switching 24 10/100/1000BASE-T Gigabit ports 8 combo SFP (mini GBIC) Stacks up to 6 DGS-3224SR switch Up to 168 Gigabit ports per stack Fail-safe star stacking architecture Redundant power supply support 160 Gbps switching fabric IP routing supporting RIP-1, RIP-2, OSPF routing protocols, DVMRP, PIM Dense mode Auto MDI/MDIX uplink for all twisted-pair ports 4K 802.1Q VLANs, IGMP snooping, eight 802.1p Priority Queues,port mirroring Multi-layer ACL and DiffServ QoS Administrator-definable port security 802.3ad Link Aggregation port trunks of up to 8 Gigabit ports Broadcast storm control 802.3x Flow Control Jumbo frame support 802.1D compatible and 802.1w Rapid Spanning Tree for redundant backup bridge paths Single IP address management per stack, SNMP v.1, v.2c, v.3 support, RMON monitoring, SYSlog, web-based management, Telnet, CLI through console port 802.1x port-based/MAC-based access control Per-port bandwidth control |
| Technical Details: | Hardware Device Ports - 24 auto-sensing 10/100/1000BASE-T ports (front panel) - 8 combo SFP (mini GBIC) ports (front panel) - 6 10Gbps stacking ports (rear panel) - 1 RS-232 console port (front panel) Unit Stacking 6 DGS-3224SR stackable switches and 1 DGS-3324SRi Stacking Master Stacking Architecture Star Port Standard/Function Support - IEEE 802.3 10BASE-T/802.3u 100BASE-TX/802.3ab 1000BASE-T - ANSI/IEEE 802.3 NWay auto-negotiation - IEEE 802.3x Flow Control - Auto MDI/MDIX - Port mirroring SFP (Mini GBIC) Support - IEEE 802.3z 1000BASE-LX (DEM-310GT transceiver) - IEEE 802.3z 1000BASE-SX (DEM-311GT transceiver) - IEEE 802.3z 1000BASE-LH (DEM-314GT transceiver) - IEEE 802.3z 1000BASE-ZX (DEM-315GT transceiver) Diagnostic LEDs Per device: - Power On/Off - Master - Console (login/POST status) - RPS in use Per 10/100/1000BASE-T port: - 1000Mbps speed, 10/100Mbps speed - Link Per SFP port: - Link/Activity Per stacking port: - Link/Activity 7-Segment Display To display unit ID in the stack Software IP Routing - IP v4 support - IP Fragmentation support - IP multi-netting - Routing protocols supported: Static routing RIP-1, RIP-2 OSPF v.2 VLAN - IEEE 802.1Q Tagged VLAN - GARP/GVRP - Asymmetric VLAN * - Number of VLANs: 4K static VLANs (max.) * - Multiple IPs per VLAN * Available in future firmware upgrade Priority Queues (CoS) - Standard: IEEE 802.1p - Number of queues: 8 Traffic Classification (CoS) Can be based on user-definable application types: - TOS - Diffserv (DSCP) - Port-based - MAC address - IP address - TCP/UDP port number Network Access Security - Port security features - 802.1x user authentication - RADIUS client - Multi-layer ACL based on: Port number TOS Diffserv (DSCP) MAC address IP address User-definable applications Spanning Tree Protocol - 802.1D Spanning Tree compatible - 802.1w Rapid Spanning Tree IP Multicast - IGMP v.2 - DVMRP - PIM Dense mode - PIM Sparse mode * * Function supported in future firmware upgrade Port Trunk - Number of ports per trunk: 8 (max.) - Number of trunks: 32 (max.) - Operation mode: load sharing - 802.3ad compatible Link Aggregation (LACP) * * Available in future firmware upgrade Performance Switch Fabric 160 Gbps Transmission Method Store-and-forward IP Address Table - 4 K host entries - 4K LPM entries MAC Address Table 16K entries per device MAC Address Learning - Dynamic entries: automatic update - Static entries: user-defined Packet Filtering/Forwarding Rates (half duplex) 1,488,100 pps per port (max.) Forwarding Rate 35.7 Mpps (excluding stacking ports) RAM Buffer 2MB per device Jumbo Frame 9,216 bytes (max.) Configuration & Management Management Support - SNMP v.1, v.2c, v.3 - Web-based management - Web GUI traffic monitoring - Web-based MAC address browsing - CLI (command line interface) - RMON monitoring - Telnet server (up to 8 sessions) - SYSLOG - ACL - DHCP/Bootp relay - DNS relay Routing Table ARP table editing supports Delete of individual IP address learned by dynamic learning MIBs - MIB-II (RFC 1213) - Bridge MIB (RFC 1493) - RMON MIB (RFC 1757) - 802.1p Priority Queues (RFC 2674) - 802.1Q VLAN MIB (RFC 2674) - IGMP MIB (RFC 2833) - If MIB (RFC 2233) - Ethernet-like MIB (RFC 1643) - RIP MIB (RFC 1724) - OSPF MIB (RFC 1850) - CIDR MIB (RFC 2096) - D-Link enterprise MIB RMON Groups 1, 2, 3, 9 (Alarm, Statistics, History, Event) IP Number Self-identification Through DHCP client, Bootp client Firmware Upgrade TFTP Console Port DB-9 RS-232 DCE Physical & Environmental Power Input 100 to 120 VAC or 200 to 240 VAC, 50/60 Hz Internal power supply Redundant Power Backup Support Connector to connect to external redundant power supply Power Consumption 90 watts (max.) Ventilation - 40 x 40 mm DC fans x 2 - 60 x 60 mm DC fans x 1 Dimensions 441 x 207 x 44 mm (device only) 19-inch rack-mount width, 1 U height Weight 3.15 kg (device only) Operating Temperature 0 to 40 (C Storage Temperature -25 to 55 (C Humidity 5% to 95% non-condensing Emission (EMI) - FCC Class A - CE Class A Safety CSA International |
| EMI/EMC Report | ( FCC No. _____ ( CE No. _________ ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No.( ) ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( Others |
| Packaging Contents: | Cable ass'y RS232, Power cord and Switch stacking cable. 1U 19 inch rack mount ear , Flat head screw M3*6 and Rubber foot. |
| UPC Code: | DGS-3324SRi/ A 790069 256042 DGS-3324SRi/E 790069 256059 DGS-3324SRi/N 790069 256066 DGS-3324SRi/U 790069 256073 DGS-3324SRi/BE 790069 256080 DGS-3324SRi/CN 790069 256097 |
| Units Per Carton: | 5 |
| Cartons Per Pallet: | 24 (Pallet C Shipping per Sea) |
| Dimensions and Weight: | Box: 550*310*92 mm, 4.5 kg Carton: 573*333*500 mm, 23.5 kg Pallet: __120*110*213____ cm, _580 kg INTRASTAT weight: 4 kg (device + accessary + manual) Packing material weight - Paper: 100 g - Plastic: g - Mixed: 3900 g (device:3100g) |