DXS-3326GSR

Date: July 13, 2004

| Product name: | 24-port SFP + 4 1000BASE-T Combo ports L3 Managed Stackable Switch and optional 2-port 10GE uplink module |
| --- | --- |
| Product Group & Type: |  |
| Revision: | A1 |
| Available: |  |
| Picture: |  |
| Why Sell This Product: | DXS-3326GSR: this is an all-fiber Gigabit switch with trendy SFP type of connections, plus combo 1000BASE-T for flexible copper Gigabit installation. It's positioned as a high-end stackable switch for enterprise solution. Part of the D-Link xStack; we give it a marketing slogan: "the Ultimate Stackable Alternative to Chassis." Meets the requirements of today's enterprise switches: Robust Availability, High Security Control, High Quality of Service. Features 10Giabit stacking and 10Gigabit uplink capability. High density fiber Gigabit (24 SFP) & L3 switching ideal for core applications. Selling Points Performance: 10Gigabit high bandwidth stacking, 10Gigabit uplink option. Availability: reliable star stacking architecture, redundant power supply support. Security & industry approach: 802.3ad Link Aggregation, 802.1D STP, 802.1W RSTP, 802.1S MSTP, RIP, OSPF, VRRP, Port/MAC based 802.1x, MAC-IP binding, Multi-layer ACL, RADIUS, TACACS+, SSH, SSL, 802.1p, DSCP, Priority queuing, Multi-layer traffic classification. High port density, cost-effective SFP fiber Gigabit slots. Stackable price, chassis function & performance. Strong D-Link xStack technical support. |
| Keyfeatures: | High port density per switch, with copper Gigabit, SFP fiber Gigabit support Very high-speed 10G uplink option 10 times faster than Gigabit Fault tolerant star stacking Up to 6 units per stack, maximum 168 Gigabit ports per stack (star stacking) Up to 12 units per stack, maximum 288 Gigabit ports per stack (ring stacking) High bandwidth 120Gbps star stacking, 40Gbps ring stacking Wire-speed packet routing supporting RIP v.1, v.2, OSPF, DVMRP, PIM Dense mode Per-port bandwidth control & multi-layer (L2, L3, L4) QoS/CoS Advanced Access Control Lists (ACL), enhanced TACACS/TACACS+ and RADIUS authentication 802.3ad Link Aggregation port trunks Jumbo frame support High availability with redundant power supply, Spanning Tree support Single IP Management, SNMP v.1, v.2c, v.3 support, RMON monitoring, Syslog, web-based management, Telnet, CLI through console port * D-Link SIM (Single IP Management) support for xStack available in firmware upgrade in the near future. |
| Technical Details: | Hardware Device Ports - 24 SFP - 4 Combo 10/100/1000BASE-T Gigabit ports - 2 10Gigabit stacking ports - 1 open slot - 1 console port Port Standard/Function Support - IEEE 802.3 10BASE-T/802.3u 100BASE-TX/802.3ab 1000BASE-T - ANSI/IEEE 802.3 NWay auto-negotiation - IEEE 802.3x Flow Control - Auto MDI/MDIX - Port mirroring SFP Support - IEEE 802.3z 1000BASE-LX (DEM-310GT transceiver) - IEEE 802.3z 1000BASE-SX (DEM-311GT transceiver) - IEEE 802.3z 1000BASE-LH (DEM-314GT transceiver) - IEEE 802.3z 1000BASE-ZX (DEM-315GT transceiver) XFP Support IEEE 802.3ae compliant transceiver Maximum Number of Units per Stack Star stacking 6 units, ring stacking 12 units * * Star stacking requires a DGS-3324SRi Stacking Master. Stacking Port Speed 20,000Mbps full-duplex per port Switch Fabric 128Gbps Packet Forwarding Rate 95Mpps Packet Buffer Memory 2MB Maximum IP Address Table Entries All models: 3K Maximum MAC Address Table Entries All models: 16K Software IP Routing - IP v.4 support - IP Fragmentation support - Multiple IP interfaces per VLAN * - Routing protocols supported: Static routing RIP v.1, RIP v.2 OSPF v.2 * * Function available in future firmware upgrade VLAN - Port-based VLAN - IEEE 802.1Q Tagged VLAN - GARP/GVRP - Maximum number of VLANs Dynamic: 255 Static: 4K Priority Queues (CoS) - Standard: IEEE 802.1p - Maximum number of queues: 8 Traffic Classification (CoS) Can be based on user-definable application types: - TOS - Diffserv (DSCP) - Port-based - MAC address - IP address - TCP/UDP port number Access Security - 802.1x port-based access control - 802.1x MAC-based access control - Port security - SSH * - SSL * * Functions available in future firmware upgrade Access Control List Multi-layer ACL based on: - MAC address - TOS - Diffserv (DSCP) - IP address - Packet protocol type - TCP/UDP port number (user-definable application types) - TCP/UDP payload (user-definable packet content) - Per port ACL definition Spanning Tree Protocol - 802.1D Spanning Tree compatible - 802.1w Rapid Spanning Tree - 802.1s Multiple Spanning Tree * * Function available in future firmware upgrade IP Multicast - IGMP v.2 - DVMRP - PIM Dense mode - VRRP * * Function supported in future firmware upgrade Port Trunk - Maximum number of ports per trunk: 8 - Maximum number of trunks per stack: 32 - Operation mode support: load sharing - 802.3ad compatible Link Aggregation (LACP) Transmission Method Store-and-Forward Jumbo Frame 9KB (max.) Configuration & Management Management Support - D-Link SIM (Single IP Management) * - SNMP v.1, v.2c, v.3 - Web-based management - Web GUI traffic monitoring - Web-based MAC address browsing - CLI (command line interface) - RMON monitoring - Telnet server (up to 8 sessions) - TACACS/TACACS+ authentication on switch admin access - RADIUS authentication on switch admin access - SYSLOG - DHCP/Bootp relay - DNS relay - Dual Images - Back-Door function - Port description - CPU utilization monitoring MIBs - MIB-II (RFC 1213) - Bridge MIB (RFC 1493) - RMON MIB (RFC 1757) - 802.1p Priority Queues (RFC 2674) - 802.1Q VLAN MIB (RFC 2674) - IGMP MIB (RFC 2833) - If MIB (RFC 2233) - Ethernet-like MIB (RFC 1643) - RIP MIB (RFC 1724) - OSPF MIB (RFC 1850) - CIDR MIB (RFC 2096) - D-Link enterprise MIB RMON Groups 1, 2, 3, 9 (Alarm, Statistics, History, Event) IP Number Self-identification Through DHCP client, Bootp client Firmware Upgrade TFTP Power Supply - 100 to 120VAC, 200 to 240VAC, 50/60Hz - Internal universal power supply - Optional external redundant power supply support Emission (EMI) - FCC Class A - CE Class A Safety CSA International Optional Redundant Power Supply DPS-500 140-watt redundant power supply DPS-800 2-slot redundant power supply chassis DPS-900 8-slot redundant power supply chassis |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( Others white box |
| Packaging Contents: | One DXS-3326GSR Device One set accessory including 2 Rack mount ear/4 Rubber feet and 8 Screws One AC power cord One Cable Ass’y RS232(DB09) One Cable Infinband 4X50CM One CD Kit for User’s Guide/CLI/D-View module One CD Kit for D-View 5.1 Trial version. One Generic QIG One H/W hard copy User’s Guide |
| UPC Code: | XS3326GSA.A1: 790069 268519 XS3326GSBEA1: 790069 268502 XS3326GSCNA1: 790069 268557 XS3326GSE.A1: 790069 268526 XS3326GSN.A1: 790069 268533 XS3326GSU.A1: 790069 268540 |
| Units Per Carton: | 2 |
| Cartons Per Pallet: | Air: 12, Sea: 18 |
| Dimensions and Weight: | Box: 565 x 527 x 140 mm, 7 kg Carton: 580 x 560 x 310 mm, 14.5 kg Pallet: (by Air) 1220 x 1020 x 1250 mm(USA), 189 kg 1200 x 1100 x 1240 mm (WW), 189 kg (by Sea)1220 x 1020 x 1810 mm(USA), 276 kg 1200 x 1100 x 1800 mm (WW), 276 kg INTRASTAT weight: kg (Box) Packing material weight (Box): - Paper: kg - Plastic: kg - Mixed: kg |