Model Name

Date: 11/4/2009

| Product Name: | DWS-4026 |
| --- | --- |
| Revision: | A1 |
| Picture: |  |
| Why Sell This Product: | After two years of selling Unified Switch, D-Link sees a growing demand for higher throughput, more advanced switch features, the need for flexibility, scalability and 802.11n AP upgrade for wireless networks. DWS-4026 is D-Link’s next-generation Unified Switch with more advanced feature as well as 802.11n support. With DWS-4026, D-Link further expands its leadership in the Unified Wired and Wireless market. Following the success of DWS-3024 and 3026 models, which manage IEEE 802.11a/b/g Access Points, DWS-4026 is able to manage 802.11n Access Point, DWL-8600AP, for higher throughput, reliability and scalability. It is a full-featured Unified Switch that centrally manages up to 64 Access Points, delivering integrated wireless mobility and security for both wired and wireless users. |
| Key Features: | 24 PoE Gigabit Ports with 2 10G uplink Manages up to 64 APs per switch Supports DWL-8600AP 802.11n Dual-band Access Point. Manages up to 8 switches in one peer group Switch Clustering for single-IP management Wired and Wireless Captive Portal for robust client authentication Adaptable Wireless enables Tunnel (L3 Tunneling) and Non-Tunnel (VLAN Forwarding) Modes Seamless L2/L3 fast roaming from AP to AP AP-AP Tunnel enables client traffic to be forwarded across subnets at the edge Supports WEP, Dynamic WEP, WPA/WP2 Personal/Enterprise security Wireless Intrusion Detection System (WIDS) Rogue AP Detection, Classification and Mitigation Auto Power Adjustment and Auto Channel Selection for managed AP. Supports RIPv1/v2 dynamic routing |
| Technical Details: | Standards - IEEE 802.3, 802.3u, IEEE 802.3ab 1000BASE-T Gigabit Ethernet, 802.3z, 802.3ae compliance - Support Full-Duplex operations - IEEE 802.3x Flow Control support for Full-Duplex mode, back pressure support for Half-Duplex mode Protocol - CSMA/CD Switching Capacity - 88 Gbps Data Transfer Rates - 65.47 Mpps MAC address Table - 8K IP address Table - 128 Static Route External RPS Support - DPS-600 Physical & Environmental Max. Power Consumption 460 W Operating Temperature 0 to 40 ℃ Storage Temperature -10 to 70 ℃ Humidity - Operation: 10%-90% RH - Storage: 5% ~ 90% RH Dimensions 441mm x 389mm x 44mm |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( IC No ( Others: EN60601-1-2 |
| Safety | ( TUV No. ( UL No. ( CSA No. ( CB No. ( CE ( Others |
| Packaging Style | (Clamshell ( White Box (Gift Box Bulk (Brown Box (Others |
| Packaging Contents: | DWS-4026 device x1 AC Power Cord x 1 Console Cable x 1 Rack-mount kit (1 set) Screw for Rack-mount kit x 8 Rubber feet x 4 Generic Managed Switch Quick Installation Guide CD-ROM with Manuals Addendums for different regions |
| Country of Origin: | Taiwan |

| UPC Code: | UPC Part Number 790069 325533 BWS4026A.....A1 790069 325540 EWS4026M.....A1G 790069 325557 IWS4026A.....A1G 790069 325564 IWS4026B.....A1G 790069 325571 IWS4026E.....A1G 790069 325588 IWS4026N.....A1G 790069 331565 IWS4026Z.....A1G 790069 325595 NWS4026C.....A1G 790069 325601 TWS4026A.....A1G 458221 7052103 JWS4026J.....A1G |
| --- | --- |
| Units Per Carton: | For USA | For EU | For WW |
|  | 2pcs/carton | 2pcs/carton | 2pcs/carton |
| Cartons Per Pallet: | For USA | For EU | For WW |
|  | Air:12, Sea: 18 | Air:18, Sea: 18 | Air:12, Sea: 18 |
| Dimensions and Weight: | Box: ( 237x168x36mm (Type A) ( 168x237x53mm (Type A53) ( 225x150x75mm (Type B) (150x225x55mm (Type B1) ( 269x162x65mm (Type C) ( 274x208x68mm (Type D) ( 208x274x95mm(Type D95) ( 208x137x95mm (Type D95 half) ( 274x208x118mm (Type D1) ( 274x208x138mm (Type D2) ( 208x274x190mm (Type D4) ( 288x245x66mm (Type E) ( 245x285x82mm(Type E1) (245x285x87mm(Type E2) ( 256x356x97mm (Type F) (137x 208x 36mm (Type G) ( 208x250x68mm (Type H) (253x 274x247mm (Type I) ( Others __565x530x145mm__, 7.725 kg Device (mm / g): Device Length Device Width Device Height Device Weight 441mm 389mm 44mm 6.2930kg Carton (cm/ kg): Carton Length Carton Width Carton Height Carton Gross Weight 589mm 310mm 566mm 15.45KG Pallet (cm/ kg): Carton per Air Pallet Air Pallet PCS Air Pallet Length Air Pallet Width Air Pallet Height US 12 EU 18 WW 12 US 24 EU 36 WW 24 US 1020mm EU 1200mm WW 1200mm US 1220mm EU 1100mm WW 1100mm US 1262mm EU 1833mm WW 1267mm Carton per Sea Pallet Sea Pallet PCS Sea Pallet Length Sea Pallet Width Sea Pallet Height US 18 EU 18 WW 18 US 36 EU 36 WW 36 US 1020mm EU 1200mm WW 1200mm US 1220mm EU 1100mm WW 1100mm US 1828mm EU 1833mm WW 1833mm INTRASTAT weight: 6.575kg Packing material weight (Box): - Paper: 0.885kg - Plastic: 0.265kg - Mixed: 0kg |