| Firmware Version: | 1.16rc028 |
| --- | --- |
| Published Date: | 2014/01/06 |

Content:

Upgrading Instructions:	2

Upgrading by using Web-UI	2

New Features:	2

Changes of MIB & D-View Module:	2

Problems Fixed:	2

Known Issues:	3

Related Documentation:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| 1.15rc014 | 2012/08/13 | DAP-2310 | A1 |

# Upgrading Instructions:

D-Link AP supports firmware upgrading via Web-UI. You may download the firmware from D-Link web site http://tsd.dlink.com.tw.

## Upgrading by using Web-UI

- Connect a work station to the LAN port of Access Point.

- Open the web browser of work station and entering the IP address of the AP. The system

default IP address is 192.168.0.50.

- Enter administrator’s username and password, user name is “admin” and leave

the password field blank by default.

To update the AP's firmware, click Maintenance > Firmware and SSL Certification

# New Features:

Security enhancement

- The setting key will be saved as encryption characters

- encrypt some sensitive info of WEB & SNMP

# Changes of MIB & D-View Module:

None

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| V1.16 | Fix in open system can be save success without network key Fix in Repeater mode when SSID Visibility disabled ,Repeater can't connect to the root AP Fix in APC mode when SSID Visibility disabled ,APC can't connect to the root AP Fix in MultiSSID setting when only change the WEP Key Index, will pop up the warning message Fix “Periodical Key Change” function doesn't work Fix “MAC Clone Manual” function doesn't work Fix “MultiSSID+WEP Spec Character” STA can't be connect to Fix security can't be sync in AP Array Fix in WPA-PSK 64 hex doesn't work normally Fix in “Limit Administrator IP” for set IP in CLI and WEB Fix in “MultiSSID's Priority” function doesn’t work Fix WPA Authentication cannot work Fix WDS connect issue Fix in WDS->WPA-Personal security can't be scan Fix in VLAN -> Disable the Multi-SSID but VLAN auto disable Fix when set authentication to WPA-PSK and select autokey then use station to connect, it will show none. Fix password support ASCII when the length less than 64 Add MIB for “clientinfo tx rx byte” |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |
| V1.16 | None |

# Related Documentation:

- DAP-2310 User Manual v1.15