| Firmware Version: | 1.05rc016 |
| --- | --- |
| Published Date: | 2014/09/05 |

Content:

Upgrading Instructions:	2

Upgrading by using Web-UI	2

New Features:	2

Changes of MIB & D-View Module:	2

Problems Fixed:	2

Known Issues:	3

Related Documentation:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| V1.00rc010 | 2014/04/09 | DAP-2660 | A1 |

# Upgrading Instructions:

D-Link AP supports firmware upgrading via Web-UI. You may download the firmware from D-Link web site http://tsd.dlink.com.tw.

## Upgrading by using Web-UI

- Connect a work station to the LAN port of Access Point.

- Open the web browser of work station and entering the IP address of the AP. The system

default IP address is 192.168.0.50.

- Enter administrator’s username and password, user name is “admin” and leave

the password field blank by default.

To update the AP's firmware, click Maintenance > Firmware and SSL Certification Upload

# New Features:

Support CWM phase I feature

Upgrade OpenSSL from 0.9.8g to 0.9.8za

# Changes of MIB & D-View Module:

First Release

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| V1.05 | Fix Led still on after reboot when led status set to off Fix STA connect to AP with 11AC but in clientinfo page does not show Fix AP Client mode panic when running5GHz endurance test, Fix AP client can't scan any root AP in 2.4GHz and 5GHz band Fix Wireless Intrusion Protection 5GHz can't detect any AP Fix MIB version show wrong Fix DHCP Static Pool Settings the DNS show wrong in WIN7 STA Support weather radar channel for EU |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |
| V1.05 | None |

# Related Documentation:

- DAP-2660 User Manual v1.02