| Firmware Version: | 1.11rc040 |
| --- | --- |
| Published Date: | 2012/04/23 |

Content:

Upgrading Instructions:	2

Upgrading by using Web-UI	2

New Features:	2

Changes of MIB & D-View Module:	2

Problems Fixed:	2

Known Issues:	3

Related Documentation:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| 1.11rc040 | 2012/04/23 | DAP-2690 | A1 |

# Upgrading Instructions:

D-Link AP supports firmware upgrading via Web-UI. You may download the firmware from D-Link web site http://tsd.dlink.com.tw.

## Upgrading by using Web-UI

- Connect a work station to the LAN port of Access Point.

- Open the web browser of work station and entering the IP address of the AP. The system

default IP address is 192.168.0.50.

- Enter administrator’s username and password, user name is “admin” and leave

the password field blank by default.

To update the AP's firmware, click Maintenance > Firmware and SSL Certification Upload

# New Features:

- Update Web Redirection behavior

# Changes of MIB & D-View Module:

None

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| V1.11 | Fix Wireless stop service when too much interference in user environment. Fix ARP table overflow issue. WDS x 2 has Low throughput Fix when enable the limit administrator vlan id but the web redirection doesn't disable Fix downlink interface can't save success in traffic control Fix when IGMP Snooping enable it don't block 224.0.0.252 in Multicast Bandwidth Control & IGMP Snooping Add & Modify the commands of Multicast Bandwidth control. Fix the AP hang up when running pressure test in Web Redirect. ( about 120~150 web sessions) Fix Web authentication fail Fix Web redirect + Web authentication fail Fix LLTD packet will let br0 enter promiscuous mode, and cause memory leak. Fix in 5G band, when set the WPA/WPA2-auto-Enterprise-TKIP,the channel width should be 20MHz and gray Fix when delete the Static IP Pool, but the STA will always get the same static IP. Fix when set the wireless mode is the mixed 802.11g and 802.11b, the channel width should be the gray to 20MHz at all times. When set 802.11n only, the security-TKIP and WEP UI should be gray or would not have this item. When build the APC mode, the signal is show error. Fix in Time and Date Settings some TimeZone can't get the correct time. Fix when enable the Multi SSID and modify it, the page will show error. Fix when the HEX encrypt, set a~f, it will match upper/lower case. but when connect AP use STA, it will not match upper/lower case Fix in 11a band/WPA-PSK/Periodical Key Change :it can't show time interval in email log info Fix in 5Ghz Multi-SSID+Periodical Key Change when save and active, PassPhrase show null. Fix 20 clients connect with AP, endurance test fail. |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |
| V1.11 | None |

# Related Documentation:

- DAP-2690 User Manual v1.0