DBT-122

Date: March 14, 2005

| Product name: | USB Bluetooth Adapter |
| --- | --- |
| Revision: | A1 |
| Available: | M/ Feb. 2005 |
| Picture: |  |
| Why Sell This Product: | We’re releasing this new Bluetooth adapter to supplement our current DBT-120 Bluetooth adapter. The new DBT-122 adapter complies with the newer 1.2 Bluetooth standard, supports the Adaptive Frequency Hopping (AFH) function that resolves all channel utilization conflicts with any Wi-Fi equipment operating in the same area, and is targeted at the main Bluetooth markets such as Europe. The current DBT-120 will continue to sell in the U.S., where it has been popular. The new DBT-122 will eventually replace the DBT-120 in the future. Selling Points Works with Windows-based PCs, including Win2000 and XP. Supports Adaptive Frequency Hopping (AFH) function that automatically selects to use channels not utilized by nearby operating Wi-Fi equipment. Supports more Bluetooth profiles. |
| Key Features: | USB connection to PC Up to 723Kbps asymmetrical, 433.9Kbps symmetrical data transfer rate Bluetooth SIG 1.2 compliant Supports Adaptive Frequency Hopping (AFH) function RF wireless frequency 2400to 2483.5 MHz for USA, Europe, Japan, 2446.5 to 2483.5 MHz for France 128-bit data encryption 2dBi on-board antenna Up to 10 meters (33 ft.) wireless operation range* * Environmental factors may adversely affect operation range. |
| Technical Details: | System Requirements - PC equipped with 300MHz processor or above - 64 MB RAM or more - USB 1.1 or 2.0 port - Microsoft Windows XP, 2000, ME or 98SE with USB 1.1/2.0 support - CD-ROM drive (for device driver installation) Bluetooth Standard Bluetooth SIG 1.2 Host Interface USB 1.1 Bluetooth Profile - DUN: DT/GW - Fax: DT/GW - FTP: client/server - HCRP: client - Headset: AG/HS - HID: host - OPP: client/server - PAN: AP/group/user - SPP: Dev A/Dev B - Sync: client /server - LAN: DT/GW - Generic Access - Basic Image RF Emission Type Frequency Hopping Spread Spectrum (FHSS) RF Modulation Type GFSK RF Frequency - 2400 to 2483.5MHz for USA, Europe, Japan - 2446.5 to 2483.5 MHz for France Transmit Output Power -6 to +4dBm (Class 2) Receive Sensitivity -83 dBm typical across pass band under high interference environments Antenna 2dBi on-board General Function Supports up to 7 slave devices Transfer Rates - Up to 723 Kbps asymmetrical - Up to 433.9 Kbps symmetrical Data Encryption 128-bit Wireless Operation Range Up to 10 meters (33 feet) peer-to-peer * * Environmental factors may adversely affect operation range. Physical & Environmental Power Supply USB powered (derived from PC) Dimensions 47 x 19 x 10 mm Weight 78 grams Operating Temperature 0 to 50 ℃ Storage Temperature -20 to 65 ℃ Operating Humidity 5% to 95% non-condensing Emission Certification - FCC Class B - CE - C-Tick - VCCI - BSMI O.S. Driver Support Windows XP, 2000, ME, 98 SE Package Includes - DBT-122 USB adapter - USB extension cable - CD (containing User's Manual) - Quick Installation Guide |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( White Box with D-Link Logo ( Others |
| Packaging Contents: | DBT-122 Device USB Extension Cable CD-ROM with Mannual QIG |
| UPC Code: | BBT122….A1 790069 276040 IBT122….A1 790069 276057 IBT122SG..A1 790069 276064 EBT122….A1 790069 276071 NBT122….A1 790069 276088 TBT122….A1 790069 276095 |
| Units Per Carton: | 40 |
| Cartons Per Pallet: | For USA Air: , Sea: | For WW Air:12, Sea: 20 |
| Dimensions and Weight: | Box: ,Others , 0.27 kg Carton: 495 x 410 x 360 mm, 11.7 kg Pallet: (by Air) mm, kg (for USA) 1200 X 1100 X1230 mm, 162 kg (for WW) (by Sea) mm, kg (for USA) 1200 x 1100 x 1950 mm, 255 kg (for WW) INTRASTAT weight: 0.126 kg (Box) Packing material weight (Box): - Paper: 0.098 kg - Plastic: 0.044 kg - Mixed: 0.004 kg |