Product External Specification

For

802.11g Outdoor Access Point

Model Name: DWL-2700AP

H/W version: B

Version: 1.10

Date: 2007/8/27

Revision History

This document contains confidential proprietary information and is the property of D-Link Corporation.. The contents of this document may not be disclosed to unauthorized persons without the written consent of D-Link Corporation.

| Rev. | Date | Author | Reason for Changes |
| --- | --- | --- | --- |
| 1.0 | Jul.31, 2006 | In-Yan Chen | New released |
| 1.10 | Aug 27,2007 | Ares Ding | Revise the spec format |

# Contents

Revision History	ii

1.0 Scope	1

1.1 Description	1

1.2 Product Feature	1

2.0 Requirements	3

2.1 Hardware specification	3

2.1.1 Block Diagram	3

2.1.2 Hardware Interface	3

2.1.3 LED indicator	3

2.1.4 IEEE 802.11b Section	4

2.1.5 IEEE 802.11g Section	4

2.1.6 IEEE 802.3 Section	4

2.2 Function description	1

2.2.1 Setup	2

2.2.2 Advanced Function Configuration	4

2.2.3 Maintenance	4

2.2.4 Status	4

2.2.5 Help	5

2.3 Electrical Characteristic	5

2.4 Mechanical information	5

2.5 Compatibility Requirements	5

2.6 EMI, Safety and other certification	5

2.7 Requirements of Reliability	6

2.8 Physical Environment	6

# 1.0 Scope

## 1.1 Description

The DWL-2700AP 11g Outdoor Access Point simultaneously connects to both 802.11b/g wireless networks. The DWL-2700AP is the ideal solution for any network administrator who needs to expand the capacity of the wireless network and allow users on different frequencies to connect.

Featuring the latest 802.11g technology in 2.4GHz, it is also a best-of-both-worlds solution for those operating wireless networks in public areas where the extra bandwidth can attract additional paying customers.

DWL-2700AP is design for harsh outdoor environment. With die-cast watertight housing, this is a robust outdoor access point. Equipped with cost-effective Power-Over-Internet for supply power to the AP when a powerful outlet is not easily available and it includes the necessary hardware for mounting on a roof top or other exterior location.

At transfer rates of up to 54Mbps in the 2.4GHz frequency range, users connected to the DWL-2700AP will enjoy faster downloads and truly instant email communication.

In addition to bridging 802.11b/802.11g wireless networks, the DWL-2700AP can bridge to wired networks with its integrated 10/100M Ethernet port.

For more secure communication, the DWL-2700AP supports user-select cable encryption settings up to 152-bit WEP on the 2.4GHz band. With its web-based configuration the DWL-2700AP is easy to install, alter or activate advanced setting, or update with the latest firmware.

## 1.2 Product Feature

Device interface

LAN Ethernet Support:

One port 10/100Mbps

Complies with IEEE 802.3u specification

Support Auto Negotiation

Support Auto MDI/MDIX

Support IEEE802.3x flow control in full duplex mode

Wireless Ethernet support:

Provide Ethernet to Wireless LAN bridge fully IEEE 802.3/u compatible on the Ethernet side and fully

interoperable with IEEE 802.11b/g compliant equipment.

Compatible with IEEE 802.11b high rate standard operation at 2.4GHz frequency band to provide wireless 11Mbps

data rate.

Compatible with IEEE 802.11g high rate standard operation at 2.4GHz frequency band to provide wireless 54Mbps

data rate.

Operation at 2.4~2.5GHz frequency band to meet worldwide regulations

Dynamic date rate scaling at 1, 2, 5.5, and 11Mbps for IEEE 802.11b

Dynamic date rate scaling at 6, 9, 12, 18, 24, 36, 48, 54Mbps for IEEE 802.11g

Serial Console

One serial console  port

Functions support

LAN type support

Static IP

Dynamic IP

Modes

Supports AP , WDS, WDS with AP mode

Security

Supports IEEE 802.11 b/g wireless data encryption with 64/128/152 bit WEP for security

Supports enhanced security – AES, 802.1X, RADIUS client, and Cipher negotiation

MAC Address Filtering

Supports WMM

DHCP Server.

Web-based configuration and management

Extensive logging of AP events

# 2.0 Requirements

The following sections identify the detailed requirements of the DWL-2700AP Wireless Access Point.

## 2.1 Hardware specification

### 2.1.1 Block Diagram

### 2.1.2 Hardware Interface

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.1.2.1 | Ethernet Interface | One LAN port (10/100 Based-TX port) |
| 2.1.2.2 | Antenna Type | Two 5dbi Detachable reverse N antennas |
| 2.1.2.3 | Reset Button | Pressing the Reset Button restores the access point to its original factory default settings.(Inside, on the PCB) |
| 2.1.2.4 | Serial port | One water proof serial console port |

### 2.1.3 LED indicator

|  | LED Indicator | Color | Status | Description |
| --- | --- | --- | --- | --- |
| 2.1.3.9 | 11g | Green | Blinking Green | Wireless is ready |
|  |  |  | Light off | Wireless is off |
|  | LAN | Green | Solid Green | link up |
|  |  |  | Blink Green | Data transmission |
|  | Power | Green | Solid Green | The device is ready |
|  |  |  | Blinking Green | The device is power on |
|  |  |  | Light off | The device is power off |

### 2.1.4 IEEE 802.11b Section

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.1.4.1 | Standard | IEEE 802.11b |
| 2.1.4.2 | Radio and Modulation Schemes | DQPSK, DBPSK, DSSS, and CCK |
| 2.1.4.3 | Operating Frequency | 2400 ~ 2497MHz ISM band |
| 2.1.4.4 | Channel Numbers | 11 channels for United States 13 channels for Europe Countries |
| 2.1.4.5 | Data Rate | 11, 5.5, 2, and 1Mbps |
| 2.1.4.6 | Media Access Protocol | CSMA/CA with ACK |
| 2.1.4.7 | Maximum Transmitter Output Power | Typical 23dBm at 11, 5.5, 2, and 1Mbps |
| 2.1.4.8 | Receiver Sensitivity | Typical Sensitivity at Which Frame (1000-byte PDUs) Error Rate = 8% at room temperature. 11Mbps: Typical -84dBm @ 8% PER (Packet Error Rate) 5.5Mbps: Typical -89dBm @ 8% PER (Packet Error Rate) 2Mbps: Typical -90dBm @ 8% PER (Packet Error Rate) 1Mbps: Typical -91dBm @ 8% PER (Packet Error Rate) |

### 2.1.5 IEEE 802.11g Section

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.1.5.1 | Standard | 2.4GHz OFDM (IEEE 802.11g ) |
| 2.1.5.2 | Radio and Modulation Schemes | BPSK, QPSK, 16QAM, 64QAM, and OFDM |
| 2.1.5.3 | Operating Frequency | 2400 ~ 2497MHz ISM band |
| 2.1.5.4 | Channel Numbers | 11 channels for United States 13 channels for Europe Countries 13 channels for Japan |
| 2.1.5.5 | Data Rate | 54, 48, 36, 24, 18, 12, 9, and 6Mbps |
| 2.1.5.6 | Media Access Protocol | CSMA/CA with ACK |
| 2.1.5.7 | Maximum Transmitter Output Power | Typical 23dBm at 6~54 Mbps |
| 2.1.5.8 | Receiver Sensitivity | Error Rate = 10% at room temperature. –85dBm at 6Mbps 54Mbps: Typical -68dBm @ 10% PER (Packet Error Rate) 48Mbps: Typical -69dBm @ 10% PER (Packet Error Rate) 36Mbps: Typical -73dBm @ 10% PER (Packet Error Rate) 24Mbps: Typical -77dBm @ 10% PER (Packet Error Rate) 18Mbps: Typical -80dBm @ 10% PER (Packet Error Rate) 12Mbps: Typical -82dBm @ 10% PER (Packet Error Rate) 9Mbps: Typical -84dBm @ 10% PER (Packet Error Rate) 6Mbps: Typical -85dBm @ 10% PER (Packet Error Rate) |

### 2.1.6 IEEE 802.3 Section

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.1.6.1 | One 10/100BASE-T LAN port | Compliant to following standards, IEEE 802.3 compliance IEEE 802.3u compliance Support Full/Half Duplex operations IEEE 802.3x Flow Control support |

## 2.2 Function description

Product UI structure

| Home/Basic Settings | Home/Advanced Settings | Home/Status | Tools | Configuration | System | Logout | Help |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Wireless | Performance | Device Information | Administrator Settings | Save and Activate | System Settings |  |  |
| LAN | Grouping | Indication | Firmware and SSL | Discard Changes |  |  |  |
|  | Multi-SSID | Client Information | Configuration file |  |  |  |  |
|  | DHCP server | WDS information | SNTP |  |  |  |  |
|  | Filter | Stats |  |  |  |  |  |
|  |  | Log |  |  |  |  |  |

This web-based configuration interface includes the following functions:

- Basic Settings
It allows you to configure parameters for wireless networking and wire networking configuration.

- Advanced Settings
Advanced Function Configuration allows you to configure advanced features such as Multiple SSID, MAC filter and advanced wireless parameters.

- Status
Status allows you to display the AP information and status.

- Tools
Tools provides administrators to manage the AP.

- Configuration

Save settings or discard change

- System

Restart or factory reset AP.

- Logout

- Help
To provide an online user manual that facilitates the setup.

### 2.2.1 Home/Basic Settings

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.2.1.1 | Wireless | Wireless Band IEEE 802.11g in default Mode Access Point, WDS, WDS with AP Wireless Network Name Also called the SSID. SSID is a group of AP. SSID is the name of the WLAN used for identifying the WLAN. Default is set to “dlink” Channel Can select the radio channel. The permissible channels depends on each domain Auto Channel Select Enable/Disable supported. the default setting is “Enable”. SSID broadcast Enable/Disable Default setting is “enable”. Security Mode Open system/Key Encryption Disable Select this option to allow all wireless devices to communicate with the DWL-2700AP before they are required to provide the encryption key needed to gain access to the network. Open system/Key Encryption Enable Wired Equivalent Protocol (WEP) is a wireless security protocol for Wireless Local Area Networks (WLAN). The DWL-2700AP supports 64-bit 128bit and 152-bit WEP encryption. The WEP key format is Option for both Hex and ASCII. Shared Key This option to require any wireless device attempting to communicate with the DWL-2700AP to provide the WEP encryption key needed to access the network before they are allowed to communicate with the DWL-2700AP. Open system/Share Key With this setting both shared and open system are employed. Stations have the option of using either but must still have the correct key to decrypt data. WPA(2)-Personal/Enterprise Wi-Fi Protected Access authorizes and authenticates users onto the wireless network. WPA uses stronger security than WEP and is based on a key that changes automatically at a regular interval.When Personal is selected, your wireless clients will need to provide a Passphrase for authentication. When Enterprise is selected, you will need to have a RADIUS server on your network which will handle the authentication of all your wireless clients. Cipher Type -The DWL-2700AP support two different cipher types when WPA is used as the Security Type. These two options are TKIP (Temporal Key Integrity Protocol) and AES (Advanced Encryption Standard). Passphrase -This is what your wireless clients will need in order to communicate with your DWL-2700AP, when PSK is selected. Enter 8-63 alphanumeric characters. Be sure to write this Passphrase down as you will need to enter it on any other wireless devices you are trying to add to your network. Radius Server Settings-This means of WPA authentication is used in conjunction with a RADIUS server that must be present on your network. Enter the IP address, port, and Shared Secret that you RADIUS is configured for. You also have the option to enter information for a second RADIUS server in the even that there are two on your network which you are using to authenticate wireless clients. 802.1x- It uses a central authentication server like Remote Authentication Dial-In User Service (RADIUS) server to authenticate each user on the network. The 802.1X standard is designed to enhance the security of wireless local area networks (WLANs) that follow the IEEE 802.11 standard. 802.1X provides an authentication framework for wireless LANs, allowing a user to be authenticated by a central authority. The actual algorithm that is used to determine whether a user is authentic is left open and multiple algorithms are possible. 802.1X uses an existing protocol, the Extensible Authentication Protocol (EAP), for message exchange during the authentication process. In a wireless LAN with 802.1X, a user (known as the supplicant) requests access to an access point (known as the authenticator). The access point forces the user (actually, the user's client software) into an unauthorized state that allows the client to send only an EAP start message. The access point returns an EAP message requesting the user's identity. The client returns the identity, which is then forwarded by the access point to the authentication server, which uses an algorithm to authenticate the user and then returns an accept or reject message back to the access point. Assuming an accept was received, the access point changes the client's state to authorized and normal traffic can now take place. |
| 2.2.2.2 | LAN | Static IP Address Select this option if there is no DHCP server in your network or you want to set AP’s IP manually. Dynamic IP Address Select this option if there is a DHCP server in your network and it provides you an IP address automatically... |

### 2.2.2 Home/Advanced Settings

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.2.2.1 | Performance | Advanced Wireless Setup provides administrators to configure detail wireless perimeters. |
| 2.2.2.2 | Grouping | This option provides two functions: AP load balance by user limit and link integrate. |
| 2.2.2.3 | Multi-SSID | One primary SSID and at most 7 guests SSIDs can be configured to allow virtually segregation stations by sharing same channel. This function is supported on AP mode only. |
| 2.2.2.4 | DHCP server | DHCP (Dynamic Host Control Protocol) Server assigns IP addresses to stations requesting IP addresses while logging to the wireless network. Stations must be configured as DHCP client in order to obtain IP addresses automatically. The default value for DHCP Server control is "disable". |
| 2.2.2.5 | Filter | DWL-2700AP can be configured to deny or only allow Ethernet stations association by filtering MAC addresses. By selecting "Accept", DWL-2700AP can only be associated with MAC addresses listed in the Authorization table. By selecting "Off", this function will be turned off. |

### 2.2.3 Status

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.2.4.1 | Device Info | All of your AP details are displayed on the Device Info page. The firmware version is also displayed here. |
| 2.2.4.2 | Indication | Displays real-time data of temperature. |
| 2.2.4.3 | Client Information | Displays the associated clients SSID, MAC, Band, Authentication method, Signal strength, and Power Saving Mode for the DWL-2700AP network. |
| 2.2.4.4 | WDS Information | Displays the WDS SSID, MAC, Band, Authentication method, Signal strength, and Power Saving Mode for the DWL-2700AP network. |
| 2.2.4.5 | Stats | The Statistics page displays all of the LAN, WAN, and Wireless packet transmit and receive statistics. |
| 2.2.4.6 | Logs | The AP automatically logs (records) events of possible interest in its internal memory. If there is not enough internal memory for all events, logs of older events are deleted, but logs of the latest events are retained. The Logs option allows you to view the AP logs. You can define what types of events you want to view and the level of events to view. This AP also has external Syslog Server support so you can send the log files to a computer on your network that is running a Syslog utility. |

### 2.2.4 Tools

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.2.4.1 | Administrator Settings | The Admin option is used to set a password for access to the Web-based management. |
| 2.2.4.2 | Firmware and SSL | The Firmware Upgrade section can be used to update to the latest firmware code to improve functionality and performance. You can also upload your SSL cert. to the AP via this page. |
| 2.2.4.3 | Configuration file | You can upload and download configuration files of the access point. |
| 2.2.4.4 | SNTP | User can set the NTP setting on this page |

### 2.2.5 Configuration

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.2.5.1 | Save and Activate | This option will write the configuration to the AP and make it activate. |
| 2.2.5.2 | Discard change | This option will discard the change you made before. |

### 2.2.6 System

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.2.6.1 | System Settings | Reset the AP or factory reset the AP to default. |

### 2.2.7 Help

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.2.7.1 | Help | Online User Manual |

## 2.3 Electrical Characteristic

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.3.1 | Operating Voltage | 48VDC +/- 10% for POE |
|  | Current Consumption | Max. 7W without POE (without heater) Max. 8.5W with POE(without heater) Max. 27W without POE (with heater) Max. 28.5W with POE(with heater) |

## 2.4 Mechanical information

|  | Feature | Detailed Description |
| --- | --- | --- |
|  | Length | 277.7mm |
|  | Width | 155mm |
|  | Height | 45mm |

## 2.5 Compatibility Requirements

This device passes the following compatibility requirements.

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.5.1 | Wi-Fi | WPA/WPA2-EAP (EAP Type: TLS,TTLS,PEAP,SIM) WPA/WPA2-PSK WMM |

## 2.6 EMI, Safety and other certification

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.6.1 | United States | IEEE 802.11b/g: FCC part 15.247, 15.205, 15.209 FCC Class B Safety: UL1950-3 for CSA mark |
| 2.6.2 | Canada | IEEE 802.11b/g: Power Limits: RSS-210 6.2.2 (91) Safety: CSA |
| 2.6.3 | Europe | IEEE 802.11b/g: EMC: EN 300 328, EN 301 489-17, EN 60950 |

## 2.7 Requirements of Reliability

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.7.1 | MTBF | Mean Time Between Failure > 30,000 hours |

## 2.8 Physical Environment

|  | Feature | Detailed Description |
| --- | --- | --- |
| 2.8.1 | Operating Temperature Conditions | The product is capable of continuous reliable operation when operating in ambient temperature of -40 ℃ to +60℃. |
| 2.8.2 | Non-Operating Temperature Conditions | Neither subassemblies is damaged nor the operational performance be degraded when restored to the operating temperature after exposing to storage temperature in the range of -40 ℃ to +65 ℃. |
| 2.8.3 | Operating Humidity conditions | The product is capable of continuous reliable operation when subjected to relative humidity in the range of 10% and 90% non-condensing. |
| 2.8.4 | Non-Operating Humidity Conditions | The product is not be damaged nor the performance be degraded after exposure to relative humidity ranging from 5% to 95% non-condensing |