DWL-AG530

Date: March 8, 2004

| Product name: | 802.11a/g Wireless PCI Adapter |
| --- | --- |
| Product Group & Type: | Wireless PCI Adapter |
| Revision: | A1 |
| Available: |  |
| Picture: |  |
| Why Sell This Product: | Super AG 108Mbps high speed dualband. This DWL-AG530 card will eventually replace the current DWL-AG520 card that supports only 54Mbps speed. The DWL-AG530's Super AG 108Mbps speed is provided by means of a software driver provided on the CD. Selling Points Same price as DWL-AG520 but has higher speed. Tri-mode a/b/g, dualband wireless. Advanced security with WPA, 802.1x authentication, TKIP and Pre-Shared Key function support. |
| Keyfeatures: | 802.11a/g industry standard Dual 5GHz and 2.4GHz frequency bands Up to 108Mbps (Turbo mode) network data transfer rate on both frequency bands, 15 times faster than 802.11b Strong 64/128/152-bit WEP data encryption security Compatible with existing 802.11b wireless devices Advanced security with WPA, 802.1x authentication, TKIP and Pre-Shared Key function support Powerful integrated antenna provides 100-meter indoor,400-meter outdoor operation range * Runs Windows 98 SE, 2000, ME, XP *Environmental factors may adversely affect range |
| Technical Details: | Standards - IEEE 802.11a - IEEE 802.11b - IEEE 802.11g Bus Type - PCI 2.2 - PCI 32-bit interface Media Access Control CSMA/CA with ACK Data Rates (With automatic fallback) 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 11Mbps, 9Mbps, 6Mbps, 5.5Mbps, 2Mbps, 1Mbps Modulation Technology - Orthogonal Frequency Division Multiplexing (OFDM) - Complementary Code Keying (CCK) - Direct Sequence Spread Spectrum (DSSS) Frequency Range * - 2.4GHz to 2.5GHz - 5.15GHz to 5.875GHz * Software configurable as allowable frequency will vary from country to country in the European region. Transmit Output Power - 802.11a: +10 to 14dBm for 54Mbps +11 to 15dBm for 48Mbps +13 to 15dBm for 36Mbps +17 to 18dBm for 24, 18, 12, 9 and 6Mbps - 802.11b: +18dBm for 11, 5.5, 2 and 1Mbps - 802.11g: +10 to 14dBm for 54Mbps +11 to 15dBm for 48Mbps +13 to 15dBm for 36Mbps +17 to 18dBm for 24, 18, 12, 9 and 6Mbps Receive Sensitivity - 802.11a (@ 10% PER): -87dBm for 6Mbps -86dBm for 9Mbps -85dBm for 12Mbps -83dBm for 18Mbps -80dBm for 24Mbps -76dBm for 36Mbps -71dBm for 48Mbps -66dBm for 54Mbps -73dBm for 108Mbps (Turbo mode) - 802.11b (@ 8% PER): -84dBm for 11Mbps -90dBm for 2Mbps - 802.11g (@ 10% PER): -87dBm for 6Mbps -86dBm for 9Mbps -85dBm for 12Mbps -83dBm for 18Mbps -80dBm for 24Mbps -76dBm for 36Mbps -71dBm for 48Mbps -66dBm for 54Mbps Antenna 2dBi to 4dBi Gain omni-directional dipole antenna Operation Range - Indoors: up to 100 meters (328 feet)* - Outdoors: up to 400 meters (1,312 feet)* * Environmental factors may adversely affect range Security - 64/128/152-bit WEP data encryption - 802.1x authentication - WPA (Wi-Fi Protected Access): 802.1x, Pre Share Key, WEP, TKIP, AES Physical & Environmental LED Indicators - Power - Network Operating Voltage 5 VDC +/- 10% Power Consumption - Transmit mode: 1650mW - Receive mode: 1250mW - Sleep mode: 40mW Dimensions 133 (L) x 120 (W) x 22 (H) mm Weight 63grams Operating Temperature 0 to 45 (C Storage Temperature -10 to 60 (C Humidity 95% maximum (non-condensing) EMI Certification - FCC Class B - CE Class B O.S. Support Windows 98 SE, ME, 2000, XP |
| EMI/EMC Report | (FCC No.KA22002080002-2 (USA V.A1) ; KA22003070024-2 (USA V.A2/A3) ; KA22003070024-1 (WW V.A1) ( CE&RTTE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( Others |
| Packaging Contents: | - DWL-AG530 wireless PCI adapter - One QIG and one - CD-ROM for manual and driver. - Only provide low profile bracket for U.S.A. |
| UPC Code: | BDWLAG530.A1 790069 264375 BDWLAG530.A2 790069 264375 BDWLAG530.A3 790069 264375 BWLAG530ODA1 790069 264375 BWLAG530ODA2 790069 264375 BWLAG530ODA3 790069 264375 DWLAG530AUA1 790069 265297 DWLAG530EUA1 790069 265341 TDWLAG530.A1 790069 265358 DWLAG530SGA1 790069 265310 DWLAG530LAA1 790069 265327 DWLAG530FRA1 790069 265334 |
| Units Per Carton: | 20 |
| Cartons Per Pallet: | Air::15, Sea: 20 |
| Dimensions and Weight: | Box: 280 x 203 x 70 mm, 0.625 kg Carton: 592 x 397 x 452 mm, 14 kg Pallet: (by Air)120 x110 x 148 cm/Per Pallet A (Air) 120 x110 x 149 cm/Per Pallet C (Air) 110 x120 x 149 cm/Per Pallet E (Air) 122 x 102 x 149 cm/Per Pallet F (Air) 225 Kg/Per Pallet A (Air) 225 Kg/Per Pallet C (Air) 228.5 Kg/Per Pallet E (Air) (by Sea) 120 x110 x 192.8 cm/Per Pallet A(Sea) 120 x110 x 193.8 cm/Per Pallet C(Sea) 110 x120 x 194.3 cm/Per Pallet E(Sea) 122 x 102 x 193.8 cm/Per Pallet F(Sea) 295Kg/Per Pallet A (Sea) 295Kg/Per Pallet C (Sea) 298.5 Kg/Per Pallet E (Sea) - Paper: kg - Plastic: kg - Mixed: kg |