Procedures to install linux driver for G-520 and G-650

Please follow the procedures below:

1. At the command prompt, locate the directory where "driver.tgz" resides.

2. do the command: tar -zxvf driver.tgz   to unzip the file.

3. under the same directory, you should see a folder being unzipped name madwifi.

4. do the command: cd madwifi to go to the direcrtory

5. and do the command: make clean, then make, then make install 

6. shut down the PC and insert the wireless NIC, the system should detects the NIC

7. after reboot, at the command prompt, do the command: iwconfig, and the NIC with the name "ath0" should be in the list.

8. for non-DHCP user, do the command: iwconfig ath0 x.x.x.x to assign an IP for the NIC.

9. for non-DHCP user, do the command: vi /etc/sysconfig/network and this will bring up another window to edit the file to assign default gateway for the NIC. To edit, key in "i" to enter insert mode, after done editing, press "ESC" to leave insert mode and type :wq to save the change.

10. for non-DHCP user, do the command: vi /etc/resolv.conf to assign DNS for the NIC, the content should be something like "nameserver x.x.x.x" , after done editing, do :wq to save the change.

11.for non-DHCP user, after done editing those files, do the command: iwconfig aht0 essid "ESSID" mode Managed rate auto channel 6 key[1] 123456 (note: "ESSID" should be based on your own and it needs to be keyed capitalized; the channel number should also be based on your own and the "key" part is for if user uses WEP, if it's open system, you can skip the "key" part.)

12. do the command: iwconfig ath0 up to bring up the NIC

13. do the command: /etc/rc.d/init.d/network restart to make the changes effect.

14. for DHCP users, skip the step 8 to 10 and do the command: iwconfig ath0 up then dhclient ath0 to get an IP from the DHCP server, after that do etc/rc.d/init.d/network restart to make the changes effect.

15. try ping the AP and confirm connection.