DWL-G700AP

Date: May 18,2005

| Product name: | 802.11g/2.4GHz 54Mbps Wireless Access Piont |
| --- | --- |
| Revision: | B1 |
| Available: | E/May, 2005 |
| Picture: |  |
| Why Sell This Product: | As margins for the basic 802.11b gear is slipping, we are phasing in more 802.11g products for you to boost wireless LAN profits. This product belongs to the cost-down 802.11g AirPlusG product line, and can supplement products like DWL-G510 and DWL-G630 wireless adapters. Selling Points No 108Mbps Turbo mode, but lower cost, lower price. 54Mbps speed. More WPA and WPA2 functions added (WPA EAP, WPA PSK) |
| Key Features: | 802.11g 2.4GHz standard Up to 54Mbps wireless data transfer rates 10/100BASE-TX port for connection to Ethernet or DSL/cable modem Compatible with existing 802.11b wireless devices Built-in DHCP server for multiple user access 64/128-bit WEP data encryption WPA and the latest standard WPA2 security support Web-based configuration & management |
| Technical Details: | Network Standards - 802.11g wireless LAN - 802.11b wireless LAN - 802.3/802.3u 10BASE-T/100BASE-TX Ethernet - ANSI/IEEE 802.3 NWay auto-negotiation Media Access Control Protocol CSMA/CA with ACK Network Architecture Type Infra-structure mode Operating Frequency 2.4 to 2.4835 GHz ISM band Operating Channels - FCC: 11 - ETSI: 13 Radio and Modulation Schemes DQPSK, DBPSK, CCK, OFDM Transmit Output Power (for 802.11b) Minimum +16dBm typically Transmit Output Power (for 802.11g) Minimum +13dBm typically Security - 64/128-bit WEP data encryption - WPA EAP, WPA PSK - WPA2 AES - MAC address filtering - SSID broadcast disable function Antenna 2dBi Gain detachable external omni-directional dipole antenna with RP-SMA connector Device Management Web-based management through Internet Explorer v.6 or later, Netscape Navigator v.6 or later or other Java-enabled browser Operating Voltage 7.5VDC 1A Power Input Through external power adapter Certification - FCC Part 15.247 - ETS 300 328 |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( Brown Box ( Gift Box ( Bulk ( Others |
| Packaging Contents: | DWL-G700AP Device Detachable Antenna CAT5 Ethernet cable Power Adapter (7.5V/1A) CD with Manual QIG Mounting Kits Vertical Stand |
| UPC Code: | Part Number UPC Code EWLG700BEUB1 790069 281679 EWLG700EEUB1 790069 281686 IWLG700ANAB1 790069 281693 IWLG700BEUB1 790069 281709 IWLG700EEUB1 790069 281716 IWLG700ENAB1 790069 281723 IWLG700EISB1 790069 281730 IWLG700NEUB1 790069 281747 TWLG700ANAB1 790069 281822 NWL2K+ACEUB1 790069 281754 |
| Units Per Carton: | 10 |
| Cartons Per Pallet: | For WW by Air: 33 Sea: 44 | For EU by Air: 44 Sea: 44 |
| Dimensions and Weight: | Box: , Others mm, 1 kg Carton: 366*287*442 mm, 11 kg Pallet: (by Air) 120*110*150 cm, 378 kg (for WW) (by Sea) 120*110*195 cm, 499 kg (for WW) (by Air) 120*110*195 cm, 499 kg (for EU) (by Sea) 120*110*195 cm, 499 kg (for EU) INTRASTAT weight: 900 g (Box) Packing material weight (Box): - Paper: 80.5 g - Plastic: 15.5g - Mixed: 4 g |