# Check Your Package Contents

These are the items included with your

DWL-M60AT

    - DWL-M60AT antenna with 1.5m pig tail

    - Mounting accessories ( screw *1,

plastic anchor*1, plastic cable clamp*2 )

    - Quick installation guide

# Installing the DWL-M60AT

Step 1.	Carefully remove the antenna from the package and identify the optimal location for the antenna.

Notice: Allow the cable to bend naturally. It is recommended that you place the antenna near wireless devices to avoid excessive strain to the cable and connector

Step 2.	Place the antenna on a stable, flat surface, and use the enclosed mounting accessories to mount the antenna on the walls or ceiling.

Remove the existing antenna and start to link with DWL-M60AT..

Step3.	Adjust the antenna transmission direction to a right angle with your coin.

|  | Always place the antenna on a flat or secure surface. Concealing the antenna behind books, cabinets or other office equipment may affect the performance of the wireless networks. The antenna transmission range may vary according to different environments or applications. |
| --- | --- |

# Mounting Configurations

- When the location which is identified, fix the mounting accessories ( screw and plastic wall anchor ) into the position.

- Click the antenna base with the screw, press gently until the screw clicked into the base clip.

- Adjust the angle of the antenna to a right angle, which can attain better signal transmission and coverage area.

- In order to fix the antenna body and the base, please use coin to tighten the black fixed screw.

Installing ANT24-JC

Please use another D-Link optional jumper cable ANT24-JC to change your DWL-M60AT from RP-SMA jack to MCC.  It may allow your antenna to link with D-Link DWL-660 wireless PC card.

Please contact your reseller for D-Link optional MCC jumper cable.

# Technical Support

D-Link provides free technical support for customers within the United States during the warranty period on this product.

U.S. customers can contact D-Link Technical Support through our web site, or by phone.

D-Link Technical Support over Telephone:

- 1-800-758-5489

- 24 Hours a Day, 7 Days a Week

- 1-Year Limited Warranty from date of purchase.

D-Link Technical Support over the Internet:

- support.dlink.com

- support@dlink.com

# Text boxes

D-Link DWL-M60AT

2.4GHz Wireless Indoor Antenna

Installation Guide

Fixed screw on antenna base