# DAP-1160 Firmware Release Note

Firmware: V1.40 (build b02)

Hardware: A1

Date: 23, July, 2010

KERNEL: Linux version 2.4.18-MIPS-01.00 Wed Mar 19 15:18:35 CST 2008

Realtek Based: RTL8186 cmk 1.4c + rtl865x-sdk-1.2a kernel

WLAN Version: Mon Apr 13 11:14:57 CST 2009 by pluswang, v1.14 (2008-02-15)

CheckSum: 0x00020FC4

Problems Resolved:

- Fix bug : A buffer overflow condition can be triggered by setting

- URL filtering for an overly long URL.

- Version.txt needs login and chklst.html does not need to login

Enhancements:

NA

Firmware: V1.40 (build b01)

Hardware: A1

Date: 07, July, 2010

Firmware Version: ver2.10b02

Firmware Date: 06 Jul 2010

KERNEL: Linux version 2.4.18-MIPS-01.00 Wed Mar 19 15:18:35 CST 2008

Realtek Based: RTL8186 cmk 1.4c + rtl865x-sdk-1.2a kerne

WLAN Version: Mon Apr 13 11:14:57 CST 2009 by pluswang, v1.14 (2008-02-15)

CheckSum: 0x00027EE1

Problems Resolved:

- Fix DCC security hole : users can set and get setting or reboot from DCC protocol.

Enhancements:

NA

Firmware: v1.31b01

Hardware: A1

Date: July 15, 2009

Platform status:

- CPU BSP : RTL8186, Linux version 2.4.18-MIPS-01.00 Wed Mar 19 15:18:35 CST 2008

- WLAN DRIVER : Mon Apr 13 11:14:57 CST 2009 by pluswang, v1.14 (2008-02-15)

- Realtek Based : RTL8186 cmk 1.4c + rtl865x-sdk-1.2a kernel

- Runtime Checksum = 0x000258E4

Problems Resolved:

- Fix bug : The IPSec function in port forwarding of the Advanced page is failed.

- Fix bug : Add “Netmeeting(T.120)” in port forwarding of the Advanced page to fix when user enables Netmeeting in port forwarding, the FTP and messages are failed. (The voice is ok.)

- Fix bug : The DHCP server will be disabled after setting from wizard.

- Fix bug : The endurance with 11n client.

- Fix bug : When running TP between wlan and lan, there will be many low peak.