How to configure IPSec VPN failover

This scenario shows how both firewalls can be configured IPSec VPN failover between two WAN links. Either of WAN links is broken, all VPN traffic will be on-line redirected to other backup circuit. When the failed circuit returns to normal, these services will come back to original WAN circuit.

Detail for this scenario:

- Both firewalls are all built two WAN links for failover mechanism. One is main circuit and another one is backup circuit.

- All Traffic between Firewall A and Firewall B will be via an IPSec VPN tunnel.

1. Firewall A - Address.

Go to Objects ->Address book -> InterfaceAddresses:

Edit the following items:

Change lan_ip to 192.168.1.1

Change lannet to 192.168.1.0/24

Change wan1_ip to 192.168.110.1

Change wan1net to 192.168.110.0/24

Change wan2_ip to 192.168.120.1

Change wan2net to 192.168.120.0/24

Add a new Address Folder called RemoteHosts.

In the new folder, add following new IP Address objects

Name: fwB-IPSec-remote-net

IP Address: 192.168.2.0/24

Name: fwB-main-remote-gw

IP Address: 192.168.110.254

Name: fwB-backup-remote-gw

IP Address: 192.168.120.254

Click OK.

2. Firewall A – Pre-shared keys

Go to Objects -> Authentication Objects -> Pre-Shared keys.

Add following new Pre-Shared Key for both IPSec tunnels.

General:

Name: fwB-main-psk

Name: fwB-backup-psk

Shared secret:

Select Passphrase and enter a shared secret in above Pre-shared key objects

Click Ok.

3. Firewall A – Main IPsec interface

Create a Main IPSec Tunnel:

Go to Interfaces -> IPsec.

Add a new IPsec Tunnel for Main WAN link.

In the General tab:

General:

Name: Main-IPSec-tunnel

Local Network: lannet

Remote Network: fwB-IPSec-remote-net

Remote Endpoint: fwB-main-remote-gw

Encapsulation Mode: Tunnel

Algorithms:

IKE Algorithms: High

IKE Life Time: 28800

IPsec Algorithms: High

IPsec Life Time: 3600

IPsec Life Time: 0

Authentication:

Select Pre-Shared Key and fwB-psk.

Keep-alive:

Click Ok.

Select Auto.

Advanced:

Make sure the “Add route for remote network” option is uncheck since this route without Monitoring feature.

Click Ok.

4. Firewall A – Combine IPSec and Lan interfaces

Go to Interfaces -> Interface Groups.

Add a new InterfaceGroup :

Name: IPSec-Lan-Group

Selected Interface:

Backup-IPSec-tunnel

Main-IPSec-tunnel

Lan

Click Ok.

5. Firewall A – Rules

Go to Rules -> IP Rules.

Create a new IP Rules Folder called lan_to_fwB-IPSec

In the new folder, create a new IP Rule.

In the General tab:

General:

Name: allow_Lan_to_fwB-IPSec

Action: Allow

Service: all_services

Source Interface: IPSec-Lan-Group

Source Network: all-nets

Destination Interface: IPSec-Lan-Group

Destination Network: all-nets

Click Ok.

6. Firewall A – Manually add route for interface monitoring

Go to Routing -> Routing Tables.

Click main routing table

Add a new Route for main IPSec tunnel

In the General tab:

General:

Interface: Main-IPSec-tunnel

Network: fwB-IPSec-remote-net

Metric: 60

In the Monitor tab:

Monitor:

Make sure the “Monitor This Route” and “Monitor Interface Link Status” option is enabled.

Click Ok.

Create a second Route for backup IPSec tunnel

In the General tab:

General:

Interface: Backup-IPSec-tunnel

Network: fwB-IPSec-remote-net

Metric: 70

In the Monitor tab:

Monitor:

Make sure the “Monitor This Route” and “Monitor Interface Link Status” option is enabled.

Click Ok.

Save and activate the configuration on firewall A.

7. Firewall B - Address.

Go to Objects ->Address book -> InterfaceAddresses:

Edit the following items:

Change lan_ip to 192.168.2.1

Change lannet to 192.168.2.0/24

Change wan1_ip to 192.168.110.254

Change wan1net to 192.168.110.0/24

Change wan2_ip to 192.168.120.254

Change wan2net to 192.168.120.0/24

Add a new Address Folder called RemoteHosts.

In the new folder, add following new IP Address objects

Name: fwA-IPSec-remote-net

IP Address: 192.168.1.0/24

Name: fwA-main-remote-gw

IP Address: 192.168.110.1

Name: fwA-backup-remote-gw

IP Address: 192.168.120.1

Click OK.

8. Firewall B – Pre-shared keys

Go to Objects -> Authentication Objects -> Pre-Shared keys.

Add following new Pre-Shared Key for both IPSec tunnels.

General:

Name: fwA-main-psk

Name: fwA-backup-psk

Shared secret:

Select Passphrase and enter a shared secret in above Pre-shared key objects

Click Ok.

9. Firewall B – Main IPsec interface

Create a Main IPSec Tunnel:

Go to Interfaces -> IPsec.

Add a new IPsec Tunnel for Main WAN link.

In the General tab:

General:

Name: Main-IPSec-tunnel

Local Network: lannet

Remote Network: fwA-IPSec-remote-net

Remote Endpoint: fwA-main-remote-gw

Encapsulation Mode: Tunnel

Algorithms:

IKE Algorithms: High

IKE Life Time: 28800

IPsec Algorithms: High

IPsec Life Time: 3600

IPsec Life Time: 0

Authentication:

Select Pre-Shared Key and fwA-psk.

Keep-alive:

Click Ok.

Select Auto.

Advanced:

Make sure the “Add route for remote network” option is uncheck since this route without Monitoring feature.

Click Ok.

10. Firewall B – Combine IPSec and Lan interfaces

Go to Interfaces -> Interface Groups.

Add a new InterfaceGroup :

Name: IPSec-Lan-Group

Selected Interface:

Backup-IPSec-tunnel

Main-IPSec-tunnel

Lan

Click Ok.

11. Firewall B – Rules

Go to Rules -> IP Rules.

Create a new IP Rules Folder called lan_to_fwA-IPSec

In the new folder, create a new IP Rule.

In the General tab:

General:

Name: allow_Lan_to_fwA-IPSec

Action: Allow

Service: all_services

Source Interface: IPSec-Lan-Group

Source Network: all-nets

Destination Interface: IPSec-Lan-Group

Destination Network: all-nets

Click Ok.

12. Firewall B – Manually add route for interface monitoring

Go to Routing -> Routing Tables.

Click main routing table

Add a new Route for main IPSec tunnel

In the General tab:

General:

Interface: Main-IPSec-tunnel

Network: fwA-IPSec-remote-net

Metric: 60

In the Monitor tab:

Monitor:

Make sure the “Monitor This Route” and “Monitor Interface Link Status” option is enabled.

Click Ok.

Create a second Route for backup IPSec tunnel

In the General tab:

General:

Interface: Backup-IPSec-tunnel

Network: fwA-IPSec-remote-net

Metric: 70

In the Monitor tab:

Monitor:

Make sure the “Monitor This Route” and “Monitor Interface Link Status” option is enabled.

Click Ok.

Save and activate the configuration on firewall B.