How to configure WAN loading sharing and failover for two ISPs using policy based routing

Details for this scenario:

- WAN1 is using dynamic IP with PPPoE

- WAN2 is using a static IP

- From LAN to WAN direction on WAN1 interface, HTTP, HTTPS and FTP services are allowed to connect to Internet.

- From LAN to WAN direction on WAN2 interface, SMTP, POP3 and Ping services are allowed to connect to Internet.

WAN1 and WAN2 interface serve for different Internet services at the same time; meanwhile if any WAN circuit fails, all services will be redirected to the other WAN interface. When the failed circuit returns to normal, these services will come back to original WAN circuit.

- Addresses

Go to Objects ->Address book -> InterfaceAddresses:

Edit the following items:

Change lan_ip to 192.168.1.1

Change lannet to 192.168.1.0/24

Change wan2_ip to 192.168.120.1

Change wan2net to 192.168.120.0/24

Create a new IP address:

Name: wan2-gw

IP address: 192.168.120.254

Click Ok.

2. Ethernet interfaces

Go to Interfaces –> Ethernet:

Edit the WAN2 interface.

In the General tab:

General:

Leave IP Address as wan2_ip and Network as wan2net.

Select wan2-gw as Default Gateway.

In the Advanced tab:

Automatic Route Creation:

Deselect Add route for interface network and Add default route if default gateway is specified

Click Ok

3. PPPoE Client Configuration

Under Interfaces -> PPPoE:

Add a new PPPoE tunnel.

In the general tab:

General:

Name: PPPoEClient

Physical Interface: WAN1

Remote Network: all-nets

Authentication:

Username: dlink

Password: dlink

Confirm password: dlink

Advanced tab:

Select Add route for remote network and set Route metric to 90.

Click OK.

4. Routes

Go to Routing -> Routing Tables -> main.

Add a new Route.

In the General tab:

General:

Interface: wan2

Network: wan2net

Gateway: (None)

Local IP Address: (None)

Metric: 80

In the Monitor tab:

Monitoring for Route Failover:

Select Monitor This Route

Method:

Select Monitor Interface Link Status

Click Ok.

Add a new Route.

In the General tab:

General:

Interface: wan2

Network: all-nets

Gateway: wan2-gw

Local IP Address: (None)

Metric: 80

In the Monitor tab:

Monitoring for Route Failover:

Select Monitor This Route

Method:

Select Monitor Interface Link Status

Select Monitor Gateway Using ARP Lookup

Click Ok.

Add a new Route.

In the General tab:

General:

Interface: PPPoEClient

Network: all-nets

Gateway: (None)

Local IP Address: (None)

Metric: 90

In the Monitor tab:

Monitoring for Route Failover:

Select Monitor This Route

Method:

Select Monitor Interface Link Status

Select Monitor Gateway Using ARP Lookup

Click Ok.

5. Interface groups

Go to Interfaces -> Interface Groups.

Create a new Interface Group:

General:

Name: pppoe-wan2

Select Security/Transport Equivalent

Interfaces:

Add PPPoEClient and wan2

Click Ok

6. Rules

Go to Rules -> IP Rules.

Add a new IP Rules Folder called lan_to_pppoewan2

In the new folder, add a new IP Rule.

In the General tab:

General:

Name: allow-http-all

Action: NAT

Service: http-all

Address Filter:

Source interface: lan

Source network: lannet

Destination interface: pppoe-wan2

Destination network: all-nets

Click Ok

Now create four more rules in the same way as the first rule:

| Name | Action | Service | SourceIf | DestIf | SourceNet | DestNet |
| --- | --- | --- | --- | --- | --- | --- |
| allow-ftp | NAT | ftp-passthrough | lan | pppoe-wan2 | lannet | all-nets |
| allow-smtp | NAT | smtp | lan | pppoe-wan2 | lannet | all-nets |
| allow-pop3 | NAT | pop3 | lan | pppoe-wan2 | lannet | all-nets |
| allow-ping | NAT | ping-outbound | lan | pppoe-wan2 | lannet | all-nets |
| allow-dns | NAT | dns-all | lan | pppoe-wan2 | lannet | all-nets |

7. Policy based routing

Under Routing -> Routing Tables:

Add a new Routing Table.

General:

Name: r-pppoe

Ordering: Only

In the newly created table, add a new Route:

In the General tab:

General:

Interface: PPPoEClient

Network: all-nets

Metric: 80

Click Ok

Add a new Route:

In the General tab:

General:

Interface: wan2

Network: all-nets

Gateway: wan2-gw

Metric: 90

Click Ok

Go to Routing -> Routing Rules:

Add a new Routing Rule:

General:

Name: pbr-http-all

Forward Table: r-pppoe

Return Table: <main>

Service: http-all

Address Filter:

Source interface: lan

Source network: lannet

Destination interface: wan2

Destination network: all-nets

Click Ok

Create one more Policy-based Routing Rules in the same way as the previous one:

| Name | Forward | Return | Service | SourceIf | DestIf | SourceNet | DestNet |
| --- | --- | --- | --- | --- | --- | --- | --- |
| pbr-ftp | r-pppoe | <main> | ftp-outbound | lan | wan2 | lannet | all-nets |

Save and activate the configuration.