### DHN-120

### DHN-920

### 10 Mbps HomeLAN

### Phoneline USB Adapter

#### Quick Installation Guide

First Edition (June, 2000)

P/N 6DHN120ML.01

RECYCLABLE

Printed In Taiwan

### Introduction

This Quick Installation Guide gives step-by-step instructions for setting up the    D-Link DHN-120 or DHN-920 HomeLAN Phoneline USB adapter to connect with  your computer. The model you have purchased may appear slightly different from those shown in the illustrations. For more detailed information about DHN-120 or DHN-920,  making network connections and technical specifications, please refer to the User’s Guide included in packing .

#### Step 1 – Unpacking

Please make sure the following items are present and undamaged.

DHN-120 – include 1pcs DHN-120 device ,

1pcs USB cable & Phone cable

1pcs software CD

1pcs User’s guide

DHN-920 -  It is the conbination of the

2set DHN-120, additional

attach 1set Midpoint CD &

manual

#### Step 2 – Physical Installation

To install your Adapter you simply use the included USB cable to connect DHN-120 to an open USB port on any PC or laptop you wish to connect to the network. Please make sure that each computer is switched off before connecting to the USB port.  Once your network has been created, you will be able to hot-plug the DHN-120 at any time.  For the purposes of this manual, it is best if you initially install the adapter with your computers powered off.  Please also read the User’s guide and any safety documentation that may have come with your computer. It is important that you understand all cautions and safety measures recommended by the computer’s manufacturer before proceeding.

#### Step 2 – Installing Cables

The DHN-920 contains two normal phone cables, each 15 feet in length. If you need a longer cable, they are sold at most electronics stores. If you want to use a phone on the same phone jack, we recommend that you purchase a splitter for the jack, or use the "Phone" jack on the DHN-120 unit.

Power OFF your computer and unplug its power cord.

Locate any available USB port.  See the example below.

Gently insert the large connector of the USB cable into an open USB port on the computer.

Gently insert the small connector of the USB cable into the USB port on the DHN-120 unit.

Connect one connector of the telephone cable to the telephone jack marked "Line" on DHN-120 unit.  Connect the other end of the telephone cable to the wall jack.

If you plan to use 2 or more phone jacks, make sure that they are active and on the same line (the same telephone number or are on the same circuit).  The DHN-120   will not interfere with your normal phone, analog modem, or DSL modem.

With the power off on your computers, run the first cable from your card directly to the phone jack. If you have two available phone jacks on the same line (telephone number) then simply repeat this step for any other machines you would like to add to your home phoneline network like the picture below !

If you plan to have two computers in the same room and only have one phone jack, you can “daisy chain” the computers together. Simply run your first phoneline cable from one of the computers to an available, active phone line. Then run the second cable from the second port of the first computer to one of the ports on the second computer. Just like the picture below:

#### Step 4 – Installing Software

You have completed the hardware installation necessary to start operating your network. But, before you start sending those print jobs to the printer in the other room or start playing fast paced network games with your family, you need to tell your computers that they are connected to a network—that is, you need to install the Networking System Software. This will consist primarily of installing device drivers for your Network Adapters. Device drivers help the operating system on your computer to identify and operate devices such as printers and Network Adapters.

Networking Basics

You may have had some ideas about how to use your new network prior to installing DHN-920 – sharing files, printing from any computer on the network, or accessing the Internet on multiple computers with one connection. This section will help you get started on those ideas or even give you some new ones.

If you are interested in learning more about networking, we have identified some Internet resources that may be of interest:
 http://www.dlink.com.tw