| Firmware Version: | v1.04_4026 |
| --- | --- |
| Prom Code Version: |  |
| Published Date: | 2014/8/14 |

Content:

Upgrading Instructions:	2

New Features:	2

Problems Fixed:	2

Known Issues:	3

Related Documentation:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| v1.04_4026 | 2014/8/14 | DCS-825L | A1 |
| v1.03_3725 | 2014/4/14 | DCS-825L | A1 |
| V1.02_3427 | 2014/1/13 | DCS-825L | A1 |
| V1.01_3327 | 2013/11/29 | DCS-825L | A1 |
| V1.00 | 2013/10 | DCS-825L | A1 |

# New Features:

| Fireware Version | New Features |
| --- | --- |
| v1.04_4026 | Support EN300 328 v1.8.1. Upgrade mydlink agent to v2.0.17-B81. |
| v1.03_3725 | Correct the daylight saving time rule for (GMT+12:00) Fiji. Fix the HTTPS authentication issue for mydlink. Fix the incorrect field spelling issue of CGI /config/portal_info.cgi for mydlink. Fix the unsuitable copyright issue. Fix the incorrect SD card status issue after re-plugin SD card. Support full-duplex dgtalkie. Support command fw_upgrade for mydlink. Support Group Gets /config/portal_info.cgi for mydlink portal. |
| V1.02_3427 | Improve boot-up speed. Support high/low temperature events for mydlink. Turn up the volume of boot up music. Upgrade mydlink agent to v2.0.17-b49. |
| V1.01_3327 | Support Windows format size SD card. Support SD card with multi-partitions. Support following two behaviors while rebooting. Light on the thermal LED in Blue/Green/Red colors for 0.5 seconds, respectively. Play the boot up music if it’s enabled. Support display following items on Device Info web-page. MAC address both for AP router and AP client. Current wireless channel both for AP router and AP client. Speed up following processes. (work with v1.02 App) Boot up process for setup wizard Change user password Set date and time Set wireless configuration Enable NTP sync function with server “ntp1.dlink.com” as default. Upgrade mydlink agent to v2.0.17-b43. |

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| v1.04_4026 | Fix HTTP/HTTPS authentication issue for specific symbol password by upgrading lighttpd server. |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |

# Related Documentation:

N/A

# Upgrading Instructions:

Follow the steps below to upgrade the firmware:

1. Download the latest firmware file from the D-Link website. The file is in .bin file format.

For Windows:

Step 1

In the Control Panel, click Network and Internet.

Step 2

Click View network computers and devices.

Step 3

Make a note of the camera’s IP address.

Step 4

Open a web browser and enter “http://IP_Address/eng/admin/tools_firmware.cgi” in the address bar (where IP_Address is the IP address you made a note of in Step 3).

Step 5

If you do not already have the firmware file to use, follow the instructions on this page to download the latest file from the D-Link Support Page. Then click Browse… and locate the file. Finally, click the Upload button.

For Mac:

Step 1

Open Safari, and click Bonjour.

Step 2

Select the device you want to perform the firmware upgrade on.

Step 3

Add “/eng/admin/tools_firmware.cgi” to the address currently in the address bar and press Enter.

Step 4

If you do not already have the firmware file to use, follow the instructions on this page to download the latest file from the D-Link Support Page. Then click Browse… and locate the file. Finally, click the Upload button.