DCS-2121

Date: May 27, 2008

| Product Description: | Megapixel Wireless Internet Camera |
| --- | --- |
| Revision: | A1 |
| Availability: | 2008/5/29 |
| Picture: |  |
| Why Sell This Product: | DCS-2121 is the entry level network cameras with mega-pixel resolution for indoor surveillance applications and detail remote monitoring. Equipped with a 1.3 Mega-pixel (1280x1024) CMOS sensor delivering superior image details. |
| Key Features: | Mega-pixel (1280x1024) CMOS sensor 0.5 lux CMOS sensor can capture video in low-light environments 3GPP mobile surveillance 2-way audio SD card slot for front-end storage DI / DO interface The Motion JPEG and MPEG-4 streams simultaneous allow systems to be optimized for both image quality and bandwidth-efficiency. Support 3 profiles simultaneously WPS support |

| Technical Details: | Hardware & System Key Components / Performance Audio codec ADPCM, AMR Ethernet interface controller 10/100BaseT Sensor 1.3 Mega pixel 1/4” CMOS Sensor SDRAM 64 MBytes Flash Memory 8 Mbytes Lens 5.01mm, F2.8 Port Functions LAN 10/100BaseT ports x1 Compliant to following standards: IEEE 802.3 compliance IEEE 802.3u compliance Support Full-Duplex operations MDI/MDIX auto-negotiation 802.3x Flow Control support for Full-Duplex mode Supported IEEE 802.11g standard I/O Connector 4 pin-contact terminal block 1x input(2pins), 1x output(2pins) Audio Out 600mV Reset Button Reset to factory default (maintenance only) Power Consumption Max 6W Power Adaptor Input: 100-240VAC, 50/60Hz Output: 5VDC, 2.5A Storage SD card slot WPS Button WPS setting Software Features Feature Item Feature Detailed Description Networking Protocol IPV4, ARP, TCP, UDP, ICMP DHCP Client NTP Client (D-Link) DNS Client DDNS Client (D-Link) SMTP Client FTP Client HTTP Server Samba Client PPPoE RTP RTSP RTCP 3GPP LLTD SSL SIP UPnP-x UPnP AV Ethernet 10/100M BaseT Fast Ethernet auto negotiation Wireless WPS, WMM Wireless Security WEP, WPA-PSK, WPA2 Video Algorithm support MPEG4/MJPEG dual format compression simultaneously JPEG for still image (up to 1280 x 1024) Display type Support ActiveX, Java Multi-profile Support 3 profiles above simultaneously Features Adjustable image size and quality Time stamp and text overlay Three configurable motion detection windows Flip & mirror Resolution Up to 10 frames at 1280x1024 (MJPEG) Up to 10 frames at 1024x768 Up to 30 frames at 640x480 Up to 30 frames at 320x240 Up to 30 frames at 160x120 Digital zoom Up to 10X Min. illumination 0.5 lux@F2.8 3A control AGC, AWB, AES BLC Yes Electronic shutter 1/60(1/50)~1/15,000 sec Microphone Directional Omni-directional Frequency 50 ~ 16000Hz S/N ratio 6mm, – 40 db + 3db LED Enable/Disable Security Login authentication Default Admin ID/PWD Admin/space Firmware Upgrade failure protection Backup boot loader code OS Support Device Windows 2000 / Windows XP/ Windows Vista/ Linux/ MAC OS X10.3 or above / Pocket PC/ 3GPP Mobile Phone Utility Windows 2000 / Windows XP/ Windows Vista |
| --- | --- |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( IC No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( CB No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( Brown Box ( Others |
| Packaging Contents: | Internet Camera x 1 Power Adapter x 1 Stand/Mounting Brackets x 1 Master CD x 1 CAT-5 Ethernet Cable x 1 Quick Install Guide x 1 Antenna x 1 |
| UPC Code: | 790069 313998 ICS2121EEU...A1G 790069 314506 ICS2121BEU...A1G 790069 314773 ICS2121NEU…A1G 790069 314759 ICS2121ANA…A1G 790069 314766 ICS2121ENA…A1G 790069 314858 NCS2121CEU...A1G 790069 314797 TCS2121ANA…A1G 790069 314780 RCS2121EEU…A1G |
| Units Per Carton: | For USA | For EU | For WW |
|  | N/A | N/A | 10 |
| Cartons Per Pallet: |  |  |  |
|  | N/A | N/A | 33 |
| Dimensions and Weight: | Box: ( 237x168x36mm (Type A) ( 225x150x75mm (Type B) ( 269x162x65mm (Type C) ( 274x208x68mm (Type D) ( 274x208x118mm (Type D1) ( 274x208x138mm (Type D2) ( 288x245x66mm (Type E) , Others , 0.799 kg Carton: 1. For USA mm, kg 2. For WW 373*294*463 mm, 8.51 kg Pallet: (by Air) mm, kg (for USA) mm, kg (for EU) 1100*1200*1524 mm, 299.33 kg (for WW) (by Sea) mm, kg (for USA) mm, kg (for EU) 1100*1200*1987 mm, 392.94 kg (for WW) INTRASTAT weight: 0.4591 kg (Box) Packing material weight (Box):0.4807 - Paper: 0.2617 kg - Plastic: 0.075 kg - Mixed: 0.0032 kg |

| Approved | Checked | PM |
| --- | --- | --- |