| Firmware Version: | V1.24 |
| --- | --- |
| Prom Code Version: |  |
| Published Date: | 2015/10/14 |

Content:

Upgrading Instructions:	2

New Features:	2

Problems Fixed:	2

Known Issues:	2

Related Documentation:	2

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| V1.00 | 2011/8/1 | DCS-2230 | A1 |
| V1.10 | 2012/8/30 | DCS-2230 | A1 |
| V1.20 | 2013/06/13 | DCS-2230 | A1 |
| V1.22 | 2015/01/05 | DCS-2230 | A1 |
| V1.23 | 2015/09/11 | DCS-2230 | A1 |
| V1.24 | 2015/10/14 | DCS-2230 | A1 |

# Upgrading Instructions:

Follow the steps below to upgrade the firmware:

1. Download the latest firmware file from the D-Link website. The file is in .bin file format.

2. Log-in camera web UI and enter setup/Maintenance/Firmware upgrade

3. Click Browse… and specify the firmware file.

4. Click Upgrade. The camera starts to upgrade and will reboot automatically when the upgrade completes.

# New Features:

| Fireware Version | New Features |
| --- | --- |
| V1.00.00 | 1.New model MP FW release |
| V1.10.02 | Add the manual trigger API. Add IPv6, QoS, CoS, RTSP multicast, RTSP digest authentication Enhance FTP to establish sub directory, Recoding size change to 50MB or 60 sec., Event video clip support up to 5MB. Enhance DDNS account and password length to 63 |
| V1.20.00 | Add SNMP function |
| V1.22.00 | 1. Support EN300328 |

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| V1.20.00 | 1. Remove “guest” account. 2. RTSP authentication default enable 3. Fixed the security of UPNP. |
| V1.22.00 | 1. Fixed the security of SSL 3.0. 2. Fixed the security of getting the snapshot without authentication |
| V1.23.02 | 1.Fixed the security issue of NTPd issue 2.Fixed the security issue of tunneling RTSP streaming over HTTP 3.Fixed the Cross-Site Scripting(XSS) issue 4.Add the “CSRF” feature for fix the Cross-Site Request Forgery (CSFR) issue |
| V1.24.00 | Upgrade to new signing keys for fixing Code-Signing Key issue |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |
|  | N/A |

# Related Documentation:

N/A