| Firmware Version: | V1.04_b1 |
| --- | --- |
| Prom Code Version: |  |
| Published Date: | 2014/4/21 |

Content:

Upgrading Instructions:	2

New Features:	2

Problems Fixed:	3

Known Issues:	3

Related Documentation:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| V1.04_b1 | 2014/4/21 | DCS-931L | A1 |
| V1.03_b8 | 2014/3/19 | DCS-931L | A1 |
| V1.02_b5 | 2013/8/28 | DCS-931L | A1 |
| V1.01_b7 | 2013/5/24 | DCS-931L | A1 |

# Upgrading Instructions:

Follow the steps below to upgrade the firmware:

1. Download the latest firmware file from the D-Link website. The file is in .bin file format.

2. Log-in camera web UI and enter setup/Maintenance/Firmware upgrade

3. Click Browse… and specify the firmware file.

3. Click Upgrade. The camera starts to upgrade and will reboot automatically when the upgrade completes.

# New Features:

| Fireware Version | New Features |
| --- | --- |
| V1.04_b1 | Update mydlink agent to 2.0.17-b62 for fixing mydlink notification fail issue. |
| V1.03_b8 | Update mydlink agent to v2.0.17-b55. Support Win8.1 + IE11. Support Java 7 update 51. Change the default FTP to passive mode. Have WPS LED lightened for 10 seconds when WPS setup is successful. Modify copyright from [2012-2013] to [2012-2014]. Change camera time to [2014-01-01] by default. |
| V1.02_b5 | Update mydlink agent to v2.0.17-b28. Add user can configure interval setting for motion/sound detection of mail/ftp. |
| V1.01_b7 | Update mydlink agent to v2.0.17-b06. Update h.264 Activex to v1.0.0.12. Only allow 0-9, a-z, A-Z, “.”, “-“, “_” as the user account name. Change max video clip to 3072K bytes. |

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| V1.03_b8 | SSL Certificate will be automatically self signed (regenerated) during initial configuration/factory reset. Adjust sensor settings for video flash issue happened sometimes. Fix bad frame issue happened sometimes. Fix mydlink event timing issue of sound detection. |
| V1.02_b5 | Fixed schedule time of motion detection/sound detection incorrect issue when start time > end time. Fixed h.264 streaming issue tested on ios6. Fixed IP task will be restarted issue on DHCP renew time. Fixed OSD disappear issue. NTP source port change to port 123. |
| V1.01_b7 | Fix the problem that mydlink Agent will run twice when the camera is connecting to DIR-850L using WPS Push button. Fixed the bug that the live streaming would stop when set H.264 bit rate is 3M and watch it via Chrome/Firefox. Fixed mydlink event not work issue when change IP address. Fixed system not stable issue when enable E-mail/FTP video clip. Fixed UPnP compatibity issue with DIR-826L router Fixed E-mail/FTP cannot be started issue if motion/sound detection is enabled first. |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |

# Related Documentation:

N/A