# Product Announcement

Date: 2005/1/20

To: USA, DI, PRC

Subject: 24-Port 10/100Mpbs + 2 Combo 1000BASE-T/SFP PoE Web Smart Switch

PART NO.: BES1526A..A1, IES1526A..A1, IES1526B..A1, IES1526E..A1, IES1526N..A1, NES1526CN.A1, TES1526A..A1

### About DES-1526

DES-1526 is a 24-port 10/100M + 2 Combo 1000BASE-T/SFP Web Smart Switch, and all of its 10/100M port are with 802.3af PoE capability, which deliver power over CAT5 Ethernet cable for D-Link PoE capable wireless APs, IP Cams, IP phones or other 802.3af compliant powered devices. By working with DWL-P50 [PoE adapter], DES-1526 can include D-Link non-802.3af capable wireless APs, IP Cams and IP Phones into D-Link’s PoE solution. Also its Web GUI enable customers to perform easy and straight forward remote management.

Hardware Specifications

| Key Components |
| --- |
| Switching Capacity | 8.8Gbps |
| Max. Forwarding Rate | 6.55 million packets per second |
| Forwarding Mode | Store and Forward |
| SDRAM for CPU | 128Kbytes |
| Flash Memory | 1MB |
| LAN | 24 x 10/100BaseT ports Compliant to following standards: IEEE 802.3 compliance IEEE 802.3u compliance Support Full-Duplex operations IEEE 802.3x Flow Control support for Full-Duplex mode |
| Combo ports | 2 combo 1000Base-T/SFP ports 1000Base-T ports compliant to following standards: IEEE 802.3 compliance IEEE 802.3u compliance IEEE 802.3ab compliance Support Full-Duplex operations IEEE 802.3x Flow Control support for Full-Duplex mode SFP Transceivers Supported: DEM-310GT (1000BASE-LX) DEM-311GT (1000BASE-SX) DEM-314GT (1000BASE-LH) DEM-315GT (1000BASE-ZX) Compliant to following standards: IEEE 802.3z compliance |
| MAC Address Table | 4K |
| Packet Buffer memory | 768Kbytes |
| PoE Features |
| PoE Capable Ports | Port 1-24 |
| PoE Specification | Supplies power to PD device up to 15.4W per port, meeting IEEE802.3af standards and more sufficiently is able to provide power to PD devices Power Budget: Full power for up to 12 ports, or up to 7W for 24 ports Auto discovery feature, automatically recognize the connection of PD device and immediately sends power to it Auto disable port if the port current is over 350mA while other ports remain active Active circuit protection, automatically disables the port if there is a short while other ports remain active Provide the power following the classification below Class Usage Max power used by PD 0 Default 15.4W 1 Optional 4.0W 2 Optional 7.0W 3 Optional 15.4W 4 Reserved 15.4W DES-1526 follow the PSE pinout standard of Alternative A which is sending out power over number 1,2,3,6 pins of 8 wires of CAT5 UTP cable |

Product Features

| L2 Features |
| --- |
| 802.3ad Link Aggregation | Yes [Static Mode] [Note: SFP ports can not be trunked] |
| Port mirroring | Yes |
| VLAN |
| 802.1Q | Yes |
| VLAN Group | 64 |
| Quality Of Service |
| Priority queues number | 2 |
| Based on Port | Yes |
| 802.1p support | Yes |
| Management |
| Single IP to Manage Whole Stack | No |
| Web-GUI | Yes |
| CLI | Yes |
| Telnet | Yes |
| SNMP v1 | Yes |
| BooTP/DHCP client | Yes |

Physical and Environmental

| Physical and Environmental |
| --- |
| AC inputs: | 100-240 VAC, 50/60Hz Internal universal power supply |
| Operating Temperature: | 0 ~ 40°C |
| Storage Temperature: | -10~70°C |
| Humidity: | Operation: 10%-90% RH Storage: 5% ~ 90% RH |
| Dimensions: | 441mm(Length) x 310mm(Width) x 44mm (Depth) |
| EMI: | FCC Class A, CE Class A, VCCI Class A |
| Safety: | CUL International |

Box Includes

## One DES-1526 Device

## One set accessory including 2 Rack mount ears, 4 Rubber feet and 8 Screws

## One AC power cord

## One CD-ROM for Manual/QIG/Utility

## One hard copy QIG(BES1526A..A1 doesn’t packed with QIG)

## Ordering Information

BES1526A..A1	24-Port 10/100Mpbs + 2 Combo 1000BASE-T/SFP PoE Web Smart Switch, with USA power cord

IES1526A..A1	24-Port 10/100Mpbs + 2 Combo 1000BASE-T/SFP PoE Web Smart Switch, with DI QIG and USA power cord

IES1526B..A1	24-Port 10/100Mpbs + 2 Combo 1000BASE-T/SFP PoE Web Smart Switch, with DI QIG and UK power cord

IES1526E..A1	24-Port 10/100Mpbs + 2 Combo 1000BASE-T/SFP PoE Web Smart Switch, with DI QIG and European power cord

IES1526N..A1	24-Port 10/100Mpbs + 2 Combo 1000BASE-T/SFP PoE Web Smart Switch, with DI QIG and Australian power cord

NES1526CN.A1	24-Port 10/100Mpbs + 2 Combo 1000BASE-T/SFP PoE Web Smart Switch, with DI QIG and CN power cord

TES1526A..A1	24-Port 10/100Mpbs + 2 Combo 1000BASE-T/SFP PoE Web Smart Switch, with DI QIG and USA power cord

## Ordering Price

Please refer to the Price Book

## Lead Time:

4 ~ 5 weeks (with forecast)