# New Firmware Upgrade Procedure

Note: If the device is with old firmware as follows, please follow up the upgrade procedure to upgrade to the latest firmware.

| Model | Old F/W | The latest F/W |
| --- | --- | --- |
| DGS-1216T | V4.00.xx | V4.20.11 |
| DGS-1224T | V4.00.xx | V4.20.11 |
| DES-1228P | V1.00.xx or V1.10.xx or V1.20.xx | V1.30.08 |
| DES-1228 | V1.00.xx | V1.10.08 |
| DES-1252 | V1.00.xx | V1.10.08 |

Upgrade Procedure:

## User has to upgrade three different firmware files (FWU.hex, WSSldr.hex, FWN.hex) in order to accomplish new firmware upgraded. Please find the firmware file in the attached file as below.

File Requirement :

| General Name | DGS-1216T v.D1/D2 | DGS-1224T v.D1/D2 |
| --- | --- | --- |
| FWU.hex | 1216TFWU.hex | 1224TFWU.hex |
| WSSldr.hex | 1216Tldr.hex | 1224Tldr.hex |
| FWN.hex | DGS-1216T_DX_42010.hex | DGS-1224T_DX_42010.hex |
| Firmware File |  |  |

| General Name | DGS-1228P v.A1 | DGS-1228 v.A1 |
| --- | --- | --- |
| FWU.hex | 1228PFWU.hex | 1228FWU.hex |
| WSSldr.hex | 1228Pldr.hex | 1228ldr.hex |
| FWN.hex | DES-1228P_A1_13008.hex | DES-1228_A1_11008.hex |
| Firmware File |  |  |

| General Name | DGS-1252 v.A1 |
| --- | --- |
| FWU.hex | 1252FWU.hex |
| WSSldr.hex | 1252ldr.hex |
| FWN.hex | DES-1252_A1_11008.hex |
| Firmware File |  |

Users can upgrade firmware either through SmartConsole Utility or Web GUI, please follow up the steps as follows.

- Upgrade firmware through SmartConsole Utility (Please refer to below step. i-xi)

## Execute smart console utility

## Click Discovery button to search target switch

## Double click target switch to add to monitor list

## Click firmware upgrade button

## Click Browse button to search fwu.hex firmware file from user’s local PC

## Enter password and click start button to start firmware upgrade

## Wait for firmware upgrade complete

## Repeat step.i ~ step.vii, but choose WSSldr.hex to upgrade in step.v

## Repeat step.i ~ step.vii , but choose fwn.hex to upgrade in step.v

## 2. Upgrade firmware through Web GUI (Please refer to below step. i-vi)

## Open web GUI , clicking tool and choosing Firmware Backup & Upload

## Click browse button and choose fwu.hex firmware file from local user’s PC

## Click Upload button to start upgrade firmware

## iv.  Wait for firmware upgrade complete then restart Web GUI

## v.  Repeat step.i ~ step.iv , but choose WSSldr.hex in step.ii

## Repeat step.i ~ step.iv , but choose fwn.hex in step.ii