DGS-3324SR

Date:   Oct. 28, 2003

| Product name: | 24-port 1000Base-T with 4 SFP Combo ports L3 Managed Stackable Switch |
| --- | --- |
| Product Group & Type: | D-Link redundant power supply system |
| Revision: | A1 |
| Available: | 2003/11/14 |
| Picture: |  |
| Why Buy This Product: | More enterprise solutions: L3 switch supporting reliable star stacking architecture (used in conjunction with DGS-3324SRi), rich in functions with RPS support. Similarity in technical support: this switch uses the same firmware as many of our L2 and L3 switches, so it should be easier for you to support technically. Better altenative to DGS-3224SR L2 switch. Selling Points Supports reliable star stacking architecture. Combo 1000BASE-T/SFP GBIC, it's the trend. High port density for low cost per port. RPS is as an option does not add RPS cost to the switch itself. An improved and much better software function set. |
| Keyfeatures: | 24 10/100/1000BASE-T Gigabit ports 4 combo SFP (Mini GBIC) ports Up to 12 units per stack (ring architecture) or 6 units + 1 Stacking Master per stack (star architecture) Recoverable ring stacking or fail-safe star stacking Redundant power supply support 88Gbps switching fabric Auto MDI/MDIX uplink for all twisted-pair ports IP routing supporting RIP-1, RIP-2, OSPF routing protocols, DVMRP, PIM Dense mode 4K 802.1Q VLANs, IGMP snooping, eight 802.1p Priority Queues, port mirroring Multi-layer ACL and DiffServ QoS Administrator-definable port security 802.3ad Link Aggregation port trunks of up to 8 Gigabit ports Broadcast storm control 802.3x Flow Control Jumbo frame support 802.1D compatible and 802.1w Rapid Spanning Tree for redundant backup bridge paths Single IP address management per stack, SNMP v.1, v.2c,v.3 support, RMON monitoring, SYSlog, web-based management, Telnet, CLI through console port 802.1x port-based/MAC-based access control Per-port bandwidth control |
| Technical Details: | Hardware Device Ports - 24 auto-sensing 10/100/1000BASE-T ports (front panel) - 4 combo SFP (Mini GBIC) ports (front panel) - 2 10Gbps stacking ports (rear panel) - 1 RS-232 console port (front panel) Unit Stacking - Ring architecture: 12 units per stack - Star architecture: 6 units per stack + 1 DGS-3324SRi Stacking Master Port Standard/Function Support - IEEE 802.3 10BASE-T/802.3u 100BASE-TX/802.3ab 1000BASE-T - ANSI/IEEE 802.3 NWay auto-negotiation - IEEE 802.3x Flow Control - Auto MDI/MDIX - Port mirroring SFP (Mini GBIC) Support - IEEE 802.3z 1000BASE-LX (DEM-310GT transceiver) - IEEE 802.3z 1000BASE-SX (DEM-311GT transceiver) - IEEE 802.3z 1000BASE-LH (DEM-314GT transceiver) - IEEE 802.3z 1000BASE-ZX (DEM-315GT transceiver) Diagnostic LEDs Per device: - Power On/Off - Master - Console (login/POST status) - RPS in use/not in use Per 10/100/1000BASE-T port: - 1000Mbps speed, 10/100Mbps speed - Link/Activity Per SFP port: - Link/Activity Per stacking port: - Link/No Link 7-Segment Display To display unit ID in the stack Software IP Routing - IP v4 support - IP Fragmentation support - IP multi-netting - Routing protocols supported: Static routing RIP-1, RIP-2 OSPF v.2 VLAN - IEEE 802.1Q Tagged VLAN - GARP/GVRP - Asymmetric VLAN * - Number of VLANs: 4K static VLANs (max.) - Supports multiple IPs per VLAN * * Feature available in next firmware upgrade Priority Queues (CoS) - Standard: IEEE 802.1p - Number of queues: 8 Traffic Classification (CoS) Can be based on user-definable application types: - TOS - Diffserv (DSCP) - Port-based - MAC address - IP address - TCP/UDP port number Network Access Security - Port security features - 802.1x user authentication Port-based access control MAC-based access control * - RADIUS client - Multi-layer ACL based on: VLAN MAC address IP address Protocol type TCP/UDP port number 802.1p Diffserv (DSCP) - Other authentication protocols supported: SSH2 * TACACS * TACACS+ * SSL * * Features available in future firmware release Spanning Tree Protocol - 802.1D Spanning Tree compatible - 802.1w Rapid Spanning Tree * * 802.1w available in next firmware release IP Multicast - IGMP Snooping - IGMP v.2 - DVMRP - PIM Dense mode - PIM Sparse mode * * Function supported in future firmware upgrade MultiLink Trunking (MLT) Enables grouping of links between the switch and another switch or a server to provide higher bandwidth of up to 8 Gigabit ports with active redundant links. A multi-link is defined as trunked ports spanning multiple units of the stack for fail-safe connectivity to mission-critical servers and the network center. - Supports up to 32 trunking groups; up to 8 ports per group - Operation mode: load sharing - 802.3ad compatible Link Aggregation static mode - 802.3ad compatible Link Aggregation (LACP) * * Available in future firmware upgrade Performance Switch Fabric 88Gbps (32Mpps) Transmission Method Store-and-forward MAC Address Table 16K entries per device MAC Address Learning - Dynamic entries: automatic update - Static entries: user-defined IP Address Learning - Dynamic entries: automatic update - Supports Delete of individual IP addresses by dynamic learning Packet Filtering/Forwarding Rates (half duplex) 1,488,100 pps per port (max.) RAM Buffer 2MB per device Jumbo Frame Up to 9,216 bytes Configuration & Management Management Support - SNMP v.1, v.2c, v.3 * - Web-based management - Web GUI traffic monitoring - Web-based MAC address browsing - CLI (command line interface) - RMON monitoring - Telnet server - SYSLOG * SNMP v.3 available in next firmware release MIBs - MIB-II (RFC 1213) - Bridge MIB (RFC 1493) - RMON MIB (RFC 1757) - 802.1p Priority Queues (RFC 2674) - 802.1Q VLAN MIB (RFC 2674) - IGMP MIB (RFC 2833) - If MIB (RFC 2233) - Ethernet-like MIB (RFC 1643) - RIP MIB (RFC 1724) - OSPF MIB (RFC 1850) - CIDR MIB (RFC 2096) - D-Link enterprise MIB RMON Groups 1, 2, 3, 9 (Alarm, Statistics, History, Event) IP Number Self-identification Through DHCP client, Bootp client Firmware Upgrade TFTP Console Port DB-9 RS-232 DCE Physical & Environmental Power Input 100 to 240 VAC, 50~60 Hz Internal power supply Redundant Power Backup Support Connector to connect to external redundant power supply Power Consumption 90 watts (max.) Ventilation - 40 x 40 X10 mm DC fans x 2 - 60 x 60 X18 mm DC fans x 1 Dimensions 441 x 207 x 44 mm 19-inch rack-mount width, 1 U height Weight 3.15kg Operating Temperature 0 to 40 (C Storage Temperature -25 to 55 (C Humidity 5% to 95% non-condensing Emission (EMI) - FCC Class A - CE Class A Safety CSA International |
| EMI/EMC Report | ( FCC No. 039H048F ( CE No. _ _ ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No.( ) ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( Others |
| Packaging Contents: | Cable ass'y RS232, Power cord and Switch stacking cable. 1U 19 inch rack mount ear , Flat head screw M3*6 and Rubber foot. |
| UPC Code: | DGS-3324SR/ A 790069 262067 DGS-3324SR/E 790069 262074 DGS-3324SR/N 790069 262081 DGS-3324SR/U 790069 262098 DGS-3324SR/BE 790069 262104 DGS-3324SR/CN 790069 262111 |
| Units Per Carton: | 5 |
| Cartons Per Pallet: | 24 (Pallet C Shipping per Sea) |
| Dimensions and Weight: | Box: 550*310*92 mm, 4.5 kg Carton: 573*333*500 mm, 23.5 kg Pallet: __120*110*213____ cm, _580 kg INTRASTAT weight: 4 kg (device + accessary + manual) Packing material weight - Paper: 100 g - Plastic: g - Mixed: 3900 g (device:3100g) |