DEM-421XT

Date: November 26, 2004

| Product name: | Multi-Mode 300M 10G Transceiver (XFP) |
| --- | --- |
| Revision: | A1 |
| Available: | 2004/11/17 |
| Picture: |  |
| Why Sell This Product: | This represents the first 10Gigabit Fiber solution D-Link LAN switches: This transceiver provides short-distance 10G fiber connection for servers and switch-to-the-backbone attachment applications. This transceiver allows you to provide a complete solution for the DXS-3326GSR and DXS-3350SR Gigabit switches and their DEM-420X 10Gigabit optional module. Selling Points Standard compliance: This transceiver fits into any XFP slot of the LAN switches or their optional modules. Fully tested for guaranteed operation with the DXS-3326GSR and DXS-3350SR Gigabit switches. |
| Key Features: | Up to 300 m multi-mode fiber cable distance coverage Compliance with IEEE-802.3ae 10GBASE-SR specifications 10.3125Gbps to 10.51875Gbps transmission rates support 850nm wave length +3.3V/5V power supply support Compliant with Multi-Source Agreement (MSA) Small Form Factor Pluggable (XFP) Duplex LC connector Full duplex 802.3x Flow Control support Built-in 2-wire digital management and diagnostic interface |
| Technical Details: | Standard IEEE 802.3ae 10GBASE-SX 10Gigabit Ethernet Transceiver Type XFP (Small Form Factor Pluggable) Connector Duplex LC Data Rates 10.3125Gbps to 10.51875Gbps Wavelength 850nm Cable Type Multi-mode fiber Maximum Cable Distance Coverage 300 m Voltage +3.3V and +5.0V support Operating Temperature 0 to 70 ℃ Storage Temperature -40 to 85 ℃ Humidity 0% to 85% RH Emission - FCC Class B - CE |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( Others Generic Yellow Box |
| Packaging Contents: | DEM-421XT x 1 |
| UPC Code: | DEM421XT..A1 790069 272585 NDEM421XT.A1 790069 272592 |
| Units Per Carton: | 34 |
| Cartons Per Pallet: |  |
| Dimensions and Weight: | Box: 145 x 100 x 48 mm, 0.09 kg Carton: 362 x 312 x 265 mm, 4.1 kg Pallet: (by Air) 1200 x 1100 x mm, kg (for WW) 1200 x 1100 x mm, kg (for USA) (by Sea) 1220 x 1020 x mm, kg (for WW) 1220 x 1020 x mm, kg (for USA) INTRASTAT weight: 0.1 kg (Box) Packing material weight (Box): - Paper: 0.09 kg - Plastic: 0.007 kg - Mixed: 0.00 kg |