DGS-704 Dimensions

Unit: mm

1000Base-LX (SC) Single-Mode 30km Fiber GBIC Interface Module
The DGS-704 is a GBIC Module that can be used to connect to any GBIC Slot in Switches to provide a 1000Base-LX (SC) Single-Mode Fiber Connection that can go up to 30km in distance. It supports 3.3V Power input from GBIC Slots.

Feature Summary :

|  |  1-port GBIC Interface  1-port 1000Base-LX (SC) Single-Mode Fiber |
| --- | --- |

Technical Standards :

|  |  GBIC  IEEE 802.3z  IEEE 802.3x Flow Control |
| --- | --- |

Performance Feature :

    - 1310nm Wavelength

    - 18dB Power Budget

    - 30km Distance

    - 3.3V Power Supply

Operating Environment :
Dimensions :
65.4 x 33.64 x 10.9 mm

Operating Temperature :
0oC to 50oC 

Storage Temperature :
-25oC to 55oC 

Humidity :
5% to 95% non-condensing