DGS-703

- Product Briefs

DGS-703 is a 1-port GBIC Gigabit Ethernet Module, using for the D-Link’s Gigabit Layer 2 Layer 3 switches allow you to connect to another LAN switches, servers or Enterprise core switches.

- Product Features

  - GBIC Port Functions

- IEEE 802.3z compliance

- Support auto-negotiation for:

- 1000M operation

- Full duplex operation

- Flow control

- IEEE 802.3x compliant Flow Control support for full-duplex

- Single Mode Gigabit GBIC

- Wave length is 1310nm

- Power Budget is 10.5dB

- Support 3.3V power

- Fiber type is 9um single-mode fiber

- Maximum distance is 10km.

  - Physical & Environmental

    - Operating Temperature

- 0 - 50 °C

    - Storage Temperature

- -25 - 55 °C

    - Humidity:

5% - 95% non-condensing

DGS-704

- Product Briefs

DGS-704 is a 1-port GBIC Gigabit Ethernet Module, using for the D-Link’s Gigabit Layer 2 Layer 3 switches allow you to connect to another LAN switches, servers or Enterprise core switches.

- Product Features

  - GBIC Port Functions

- IEEE 802.3z compliance

- Support auto-negotiation for:

- 1000M operation

- Full duplex operation

- Flow control

- IEEE 802.3x compliant Flow Control support for full-duplex

- Single Mode Gigabit GBIC

- Wave length is 1310nm

- Power Budget is 18dB

- Support 3.3V power

- Fiber type is 9um single-mode fiber

- Maximum distance is 30km.

  - Physical & Environmental

    - Operating Temperature

- 0 - 50 °C

    - Storage Temperature

- -25 - 55 °C

    - Humidity:

- 5% - 95% non-condensing

DGS-707

- Product Briefs

DGS-707 is a 1-port 1000BASE-SX GBIC Module, using for the D-Link’s Gigabit Layer 2 Layer 3 switches allow you to connect to another LAN switches, servers or Enterprise core switches.

- Product Features

  - GBIC Port Functions

- IEEE 802.3z compliance

- Support auto-negotiation for:

- 1000M operation

- Full duplex operation

- Flow control

- IEEE 802.3x compliant Flow Control support for full-duplex

- Multi Mode Gigabit GBIC

- Wave length is 850nm

- Power Budget is 8.5dB

- Support 3.3V power

- Fiber type is 50um or 62.5um multi-mode fiber

- Maximum distance is 550m

  - Physical & Environmental

    - Operating Temperature

- 0 - 50 °C

    - Storage Temperature

- -25 - 55 °C

    - Humidity:

- 5% - 95% non-condensing

DGS-708

- Single Mode Gigabit GBIC

- Wave length is 1550nm

- Power Budget is 23dB

- Support 3.3V and 5V power

- Fiber type is 9um single-mode fiber

- Maximum distance is 70km.

  - Physical & Environmental

    - Operating Temperature

- 0 - 50 °C

    - Storage Temperature

- -25 - 55 °C

    - Humidity:

- 5% - 95% non-condensing