DPH-120S

Date: March 9, 2005

| Product name: | VoIP Phone |
| --- | --- |
| Revision: | A1 |
| Available: | E/ Mar. 2005 |
| Picture: |  |
| Why Sell This Product: | This Internet telephone supplements our recently released DPH-140S Internet telephone. It has just a fewer keyboard functions than the DPH-140S, but otherwise, all the main functions and Internet telephone protocols are the same. The new DPH-120S is slightly smaller, lighter and cheaper than the DPH-140S. With this new Internet telephone added to your product range, you should have more flexible options to offer to your service providers. Target users: home and business users wishing to make broadband Internet phone calls directly from a telephone set rather than from a computer. The older DPH-80 and DPH-100 IP phones will eventually be phased out and replaced by this new Internet telephone. Selling Points Most complete call function support from a telephone keyboard. Fully tested and available now. The D-Link name as an established supplier of Internet phone equipment. Excellent price/function ratio. |
| Key Features: | IP Telephone for broadband Internet or IP networks SIP protocol support Connects to Internet through LAN or directly to DSL or cable modem Second connection to PC IP address assignment using PPPoE, DHCP or static configuration Voice activity detection/comfort noise generation Adaptive jitter buffer Acoustic echo cancellation DTMF tone generation Easy-to-use setup/programming interface Remote software update support 2 x 16 LCD display Adjustable speaker/ringer volume control |
| Technical Details: | General WAN Connection Support Through 10/100BASE-TX Ethernet port Internet Support - IP, TCP, UDP, ARP, HTTP protocols - DHCP client - DNS VoIP Protocol Support SIP Echo Cancellation Ethernet - IEEE 802.3 10BASE-T Ethernet - IEEE 802.3u 100BASE-TX Fast Ethernet - ANSI/IEEE 802.3 NWay auto-negotiation Number of Ethernet Ports - 1 RJ-45 auto-sensing 10/100Mbps to DSL/cable modem or LAN with Internet connection - 1 RJ-45 auto-sensing 10/100Mbps to PC Audio Code - G.7.11u-law/a-law - G.723.1 - G.729a/b AEC (Acoustic Echo Cancellation) G.168 Phone Set Function Support - Redial - Menu - Mute - Transfer - Hold - Voice mail - 3-way conference - Speaker - Address book (200 records) - Special dial (10 records) - Review address records - Speaker/ringer volume adjust Tone - DTMF - Ring tone (4 selectable ring tones) - Ring back tone - Dial tone - Busy tone Key Pad - 0 to 9 keys, * key, # key - Function keys: mute, transfer, redial, hold, 3-way conference, voice mail - Others: speed dial setting, phone book, menu, OK, Cancel and Navigation keys Network Assignment - PPPoE - DHCP - Static IP Firmware Upgrade - TFTP - Auto/manual provisioning system Configuration Support - Keypad & LCD - Web browser - Auto/manual provisioning system Physical & Environmental LED Indicators - Line status - Incoming call - Speaker status Power Input 5V DC 2A AC power adapter Power Consumption 5 watts (max.) Dimensions 210 (L) x 208 (W) x 38 (H) mm Weight 635grams Operating Temperature 0 to 40 ℃ Storage Temperature -20 to 60 ℃ Operating Humidity 20% to 80% non-condensing EMI - FCC Class B - CE Class B Safety CB (IEC60950) |
| EMI/EMC Report | (FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( White Box with D-Link Logo ( Others |
| Packaging Contents: | DPH-120S Device X 1 Power Adapter X 1 CD X 1 Quick Installation Guide x 1 CAT5 Ethernet cable x 1 |
| UPC Code: | NPH120SC..A1 790069 274770 IPH120SN..A1 790069 274787 IPH120SE..A1 790069 274794 IPH120SB..A1 790069 274800 EPH120SE..A1 790069 274817 EPH120SB..A1 790069 274824 DPH120SA..A1 790069 274138 |
| Units Per Carton: | 10 |
| Cartons Per Pallet: | For WW Air: 12, Sea: 20 | For USA Air: 12, Sea: 20 |
| Dimensions and Weight: | Box: ,Others , 1.3586 kg Carton: 515x378x336 mm, 14.588 kg Pallet: (by Air) 1200 x 1100 x 1133 mm, 190 kg (for WW) 1220 x 1020 x 1133 mm, 191 kg (for USA) (by Sea) 1200 x 1100 x 1805 mm, 307 kg (for WW) 1220 x 1020 x 1805 mm, 308 kg (for USA) INTRASTAT weight: 1.0973 kg (Box) Packing material weight (Box): - Paper: 0.2445 kg - Plastic: 0.0162 kg - Mixed: 0.0006 kg |