| Firmware Version: | 1.06rc020 |
| --- | --- |
| Published Date: | 2015/07/09 |

Content:

Upgrading Instructions:	2

Upgrading by using Web-UI	2

New Features:	2

Changes of MIB & D-View Module:	2

Problems Fixed:	2

Known Issues:	3

Related Documentation:	3

Revision History and System Requirement:

| Firmware Version | Date | Model | Hardware Version |
| --- | --- | --- | --- |
| 1.02rc017 | 2015/02/05 | DAP-2330 | A1 |

# Upgrading Instructions:

D-Link AP supports firmware upgrading via Web-UI. You may download the firmware from D-Link web site http://tsd.dlink.com.tw.

## Upgrading by using Web-UI

- Connect a work station to the LAN port of Access Point.

- Open the web browser of work station and entering the IP address of the AP. The system

default IP address is 192.168.0.50.

- Enter administrator’s username and password, user name is “admin” and leave

the password field blank by default.

To update the AP's firmware, click Maintenance > Firmware and SSL Certification Upload

# New Features:

Support CWM v1.02

1.	Disassociation supported on multi-SSID

2.	Support Captive portal customization

3.	Support config file upload from CWM

# Changes of MIB & D-View Module:

CWM_DAP2330 v1.06-R16

# Problems Fixed:

| Firmware Version | Problems Fixed |
| --- | --- |
| V1.06 | Fixed issue of client can’t access the Internet when Ethernet to WLAN disable Modify timezone. Fix captive portal on other SSID(including 5G primary and MSSID) will not work when captive portal on 2.4G primary SSID is not enabled |

# Known Issues:

| Firmware Version | Known Issues |
| --- | --- |
| V1.06 | None |

# Related Documentation:

- DAP-2330 User Manual v1.03