### DWL-2100AP Firmware Release Notes

Firmware: v2.50

Hardware: A4

Date: 08/10/28

Problems Resolved:

- [FW] AP can't send standard traps.

- [FW] rogue ap list should not be shown if band is not selected.

- [APM] rogue ap list shows wrong.

- [WEB] It can't reset data rate settings

- [FW] The trap status and server ip can not be set.

- [FW] When AP mode is wds with ap, there is a lack of some logs on Syslog.

- [FW] use the wizard to configure the AP ,and set the password empty, then restart AP. the username will be changed from admin to empty

- [FW] Something wrong with the help document

- [FW] There is no image but update success by tftp.

- [FW] Intel WiFi Link 4965AGN can’t connect to AP if authentication is WPA/WPA2 PSK, and vlan state is enabled.

Enhancements:

- [FW] Modify GUI "11g only disable/enable" to "Wireless B/G Mode Mixed/11b only/11g only"   default value will be "Mixed", support CLI command.

- [FW] Support primary SSID with VLAN tag function.

- [FW] Support administration VLAN(Manage VLAN) , administrate AP with WLAN and management IP range function.

- [FW] Support WMM over WDS function.

- [FW] Support IGMP Snooping (v1/v2) function.

- [FW] Data Rate Control follows Dlink new spec.

- [FW] Support IAPP (fast roaming)

- [FW] Support Secondary RADIUS server setting

- [FW] Enable/Disable ping to AP

- [FW] Support Acct-Interim-Interval attribute for Accounting function,

- [FW] Trap server, settings(categorize the types of traps)

- AP status on UI

  - CPU and Memory utilization

  - Statistics for Ethernet TX and RX,bytes and packets

- [CLI] CLI command to input SNMP Location.

- [CLI] Hide the commands, get targetPower/gett controlPower/get swPower ,in CLI

- [CLI]Open 3 RSTP commands, rstp getstp/rstp getstate/rstp setstate

---------------------- END ----------------------