DWL-2700 AP Firmware Release Note

Firmware: v3.10r0112

Hardware: B1

Date: July 6, 2007

Code Base:

moonlight.v465-3

Tornado.v008

Problem Resolved:

1.	Fixed: Can't use the MD5 authentication on pure 802.1x/static.

2.	Setting changes: RTS Range is 1 to 2346 when WDS mode, 256 to 2346 when AP mode

3.	Fixed the bug that username max. length is 64 and password is not null, web can't login.

4.	Fixed the STA roaming problem. 2 STAs are in the same BSS and ping each other, once one of the STA roaming to another BSS. Ping will fail.

5.	Fixed Telnet can’t timeout issue when receiving half of the 3-way handshake packet.

6.	Fixed the WPA-PSK/WPA2-PSK function fail in AP and WDS mode.

7.	Fixed WEB can't get the DNS IP when AP in DHCP client mode.

8.	Fixed No System log event received anymore, after remove remote syslog server IP.

9.	Fixed Multicast packet and Broadcast while disable "Ethernet to WLAN Access" function.

10.	Fixed bugs -- system won’t check username and password when accessing WEB Help page directly.

11.	Fixed bug -- STA can't connect to Guest-SSID with WPA-PSK as below status, 	a..Primary-SSID security is Open-Sys or Share-Key.

b. Guest-SSID security is WPA(2)-PSK

12.	Fixed bug --Can't create WPA(2)-PSK in the WDS/WDSwithAP environment, and got error auth type when get association on console.

13.	Fixed bug --Send IGMP(64 bytes, multicast packet) for 30 Min ( 5000 packet/sec )and AP hang up(memory leak). Broadcast packet (arp request) also has the same bug.

14.	Fixed bug -- WDS compatibility issue(Can't connect to 8200 with WDS mode with WPA-PSK.)

15.	Fixed WDS auto-reboot issue

16.	Fixed few WEB security holes. Will deny un-authorized login.

17.	Fixed SNTP display error when daylight saving enable

18.	Fixed associated more than 83 STAs AP will reboot (Current limitation of allowed connected STAs is 64.)

19.	Fixed AP auto-reboot issue with STA connecting

Enhancements:

1.	SMTP/SYSLOG/SNTP support domain name.

2.	Add firmware upgrade protection policy in WEB.

3.	8021X pass-thru for single SSID/MSSID

4.	Support RADIUS accounting

5.	Support 64 char. input for WEB login username and RADIUS account.

6.	APM II supported

7.	Implement the Radius accounting into Web UI

8.	WMM over WDS

9.	WiFi 802.11d/h certification supported

10.	Pre-authentication supported

11.	Add foolproof to prevent form inputting same IP into limit administrator IP 1 and 2.

12.	Support 64 SMTP input characters.

13.	SSID and Active time in STA information

14.	Change the string �SSID� into �Wireless Network Name (SSID)�

15.	Add DHCP Server