DWL-3200AP

Date: May 13, 2005

| Product name: | 802.11g/2.4GHz AirPremier Managed Access Point |
| --- | --- |
| Revision: | A1 |
| Available: | M/May 2005 |
| Picture: |  |
| Why Sell This Product: | We’re introducing this wireless product as the first enterprise-class AP from D-Link to expand our current AirPremier product line. Its aim is to improve your products’ margin and to supplement your other wireless product sales. This product includes advanced management functions and is targeted at business users, hospitals, schools, convention centers and public hot spots. This AP is used for indoor installation. Selling Points High 108Mbps wireless speed and high Gain antennas. Full wireless security and management functions, including PoE, 802.1Q VLAN (multiple SSID) and WPA2 support. Manageable from SNMP D-View (available later). Can also be installed as a wireless bridge. |
| Key Features: | For Business-Class Environments Sturdy Metal Chassis Ideal for Indoor Deployments Plenum-Rated Housing Two 5dBi High-Gain Antennas Multiple Operation Modes Access Point Point-to-Point (PtP) Bridge Point-to-Multipoint (PtMP) Bridge High Performance Connectivity 802.11g Wireless Speeds Up to 54Mbps Wireless Data Transfer Rates* D-Link 108G Technology 108Mbps Wireless Speed Trusted Security Features 64/128/152-bit WEP Data Encryption WPA Personal WPA Enterprise 802.1x User Authentication AES 802.1Q Multiple SSIDs/Network Segmentation MAC Address Filtering 802.11i-Ready Convenient Installation Built-in 802.3af Power over Ethernet Locking Brackets Included Advanced Management AP Manager Web Browser (HTTP) Telnet SNMP v.3 * Maximum wireless signal rate based on IEEE standard 802.11g specifications. Actual data throughput will vary. Network conditions and environmental factors lower actual data throughput rate. |
| Technical Details: | Standards - IEEE 802.11b - IEEE 802.11g - IEEE 802.3 - IEEE 802.3u - IEEE 802.3af Data Rates - For 802.11g: 108, 54, 48, 36, 24, 18, 12, 9 and 6Mbps - For 802.11b: 11, 5.5, 2 and 1Mbps Wireless Frequency Range 2.4GHz to 2.4835GHz Antennas Dual 5dBi Gain detachable diversity dipole antennas with reverse SMA connectors Operation Modes - Access Point - Point-to-Point (PtP) Bridge - Point-to-Multipoint (PtMP) Bridge Security - 64-, 128-, 152-bit WEP data encryption - MAC address filtering - WPA/WPA2 EAP - WPA/WPA2 PSK - 802.1x User Authentication - AES - 802.11i-ready - 802.1Q SSID broadcast enable/disable - Multiple SSIDs (maximum 4) Device Management - Web-based: Internet Explorer v.6 or later; Netscape Navigator v.7 or later; or other Java-enabled browsers. - Telnet - AP Manager - SNMP v.3 Certifications - FCC Class B - CE - Wi-Fi |
| EMI/EMC Report | (FCC No. KA2DWL3200APA1 ( CE No. ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. E164374 ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( White Box with D-Link Logo ( Others (BROWN BOX) |
| Packaging Contents: | DWL-3200AP Device CAT5 Ethernet cable Power Adapter/Cord Two detachable antennas CD-ROM with Mannual QIG Wall mounted kit |
| UPC Code: | BWL3200ANAA1 790069 273544 TWL3200ANAA1 790069 273476 CWL3200ANAA1 790069 273544 EWL3200BEUA1 790069 273568 EWL3200EEUA1 790069 273575 IWL3200ANAA1 790069 273582 IWL3200EEUA1 790069 273599 IWL3200ENAA1 790069 273421 IWL3200NEUA1 790069 273438 IWL3200IS.A1 790069 281341 NWL3200CEUA1 790069 273452 |
| Units Per Carton: | 5 |
| Cartons Per Pallet: | For USA Air: 30, Sea:48 | For WW Air:30, Sea:48 For UK Air: 48, Sea:48 |
| Dimensions and Weight: | Box: ,Others , 1.843 kg Carton: 620*300*250 mm, 9.50 kg Pallet: (by Air) 1220*1020*1380 mm, 290.5 kg (for USA) _1100*1200*1380 mm, 305 kg (for WW) _1100*1200*2140 mm, 497 kg (for UK/EU) (by Sea)1220*1020*2130 mm, 455.2 kg (for USA) _1100*1200*2140 mm, 497 kg (for WW) _1100*1200*2140 mm, 497 kg (for UK/EU) INTRASTAT weight: 1.498 kg (Box) Packing material weight (Box): - Paper: 0.320 kg - Plastic: 0.0214 kg - Mixed: 0.0034 kg |

| PMA |
| --- |
| Product Class |  |
| Item Group |  |  |
| Sub Group |  |
| Intelligence |  |
| Tech.(Features) |  |
| Layer |  |  |
| Application |  |
| Q'ty |  |  |
| Interface |  |  |
| Net Interface |  |  |
| Port NO. |  |  |
| Interface |  |  |
| Net Interface |  |  |
| Port NO. |  |  |