DUB-CR200

Date: October 20, 2004

| Product name: | USB 2.0 3 port Hub with card reader |
| --- | --- |
| Product Group & Type: | USB |
| Revision: | A1 |
| Available: |  |
| Picture: |  |
| Why Sell This Product: | Target users: PC users with digital cameras and USB devices like printers, external hard drives, etc. Make use of existing channels to sell additional consumer products. Selling Points Good price/function. Compact, good look. |
| Key Features: | Compatible with USB 2.0/1.1 specifications 4 sockets supporting SD/MMC, Memory Stick, MS-Pro, 3.3 V Smart Media, Compact Flash, IBM MicroDrive 3 USB 2.0 Type A ports for convenient connection to digital cameras and USB peripherals Supports Hot-Swap and Plug and Play function No additional device drive needed for Windows ME, 2000, XP LED indicators for data access Power supplied by USB bus power Allows data exchange among different sockets |
| Technical Details: | Connectors - 1 USB 2.0 Type B female (to computer) - 3 USB 2.0 Type A female (to USB-supported devices) Slots 4 sockets supporting SD/MMC, Memory Stick, MS-Pro, 3.3 V Smart Media, Compact Flash, IBM MicroDrive Power Supply - DC input: 5VDC 2.5A - AC input: through external power adapter LED Indicators - Power - CF/MD - SM - MS/Pro - SD/MMC - 1, 2, 3 (for USB Type A ports) Dimensions 118 x 72 x 21 mm (device only) Weight 113 gram (device only) Emission (EMI) - FCC Class B - CE Class B Safety UL OS Support - Microsoft Windows 98SE, ME, 2000, XP - MacOS 9.x, 10.x and above Box Includes - DUB-CR200 Card Reader - External power adapter - USB 2.0 cable (1 meter) - Quick Installation Guide - CD |
| EMI/EMC Report | (FCC No. 40811403-D ( CE No. 40811403-E ( VCCI No. ( CTR-21 No. ( C-Tick No. ( A-Tick No. ( FDA No. ( R&TTE No. ( BSMI No. ( Others |
| Safety | ( TUV No. ( UL No. ( CSA No. ( Others |
| Packaging Style | ( Clamshell ( White Box ( Gift Box ( Bulk ( Others |
| Packaging Contents: | DUB-CR200 USB 2.0 cable in 6ft CD AC adapter(5V 2.5A) QIG |
| UPC Code: | IUBCR200A.A1 790069 27177 9 IUBCR200E.A1 790069 27178 6 IUBCR200N.A1 790069 27179 3 CUBCR200A.A1 790069 27180 9 TUBCR200A.A1 790069 27207 3 BUBCR200A.A1 790069 27220 2 |
| Units Per Carton: | 20 |
| Cartons Per Pallet: | Air: 18(for USA) , 24(for WW) Sea: 30(for USA&WW) |
| Dimensions and Weight: | Box: 225 x 77.5 x 150 mm, 0.6 kg Carton: 460 x 306 x 375 mm, 13 kg Pallet: (by Air) 1200 x 1100 x 1590 mm, 327 kg (for WW) 1220 x 1020 x 1595 mm, 249 kg (for USA) (by Sea) 1200 x 1100 x 2070 mm, 405 kg (for WW) 1220 x 1020 x 1885 mm, 405 kg (for USA) INTRASTAT weight: kg (Box) Packing material weight (Box): - Paper: 0.2333 kg - Plastic: 0.00244 kg - Mixed: 0.0048 kg |